| To | Mr TCHOFFO JEAN BAPTISTE Tel: +237 99934721 Fax: Email:jtchoffo@yahoo.com |
| --- | --- |
| Date | 09th, Nov, 2012 |
| From: Molly Lee Tel: +86-371-67668558 Mob: +86-13676960829 Fax: 86-371-67662768 Email: hjsales23@hongjigroup.com Google Talk: mollylcm@gmail.com MSN: mollylcm@hotmail.com Skype: mollylcm |

I:QUOTATION LIST

⑴

| Description | Model | Qty | Unit EXW-Price |
| --- | --- | --- | --- |
| Hopper | Build by yourself. |
| Vibrating feeder | ZSW-960x3800 | 1set | USD9355 |
| Jaw crusher | PEF600x900 | 1set | USD30645 |
| Belt conveyor | B800x20m | 1set | USD4840 |
| Impact crusher | PF-1214 | 1set | USD40323 |
| Belt conveyor | B800x20m | 1set | USD4840 |
| Belt conveyor | B650x22m | 1set | USD4268 |
| Vibrating screen | 3YK1860 | 1set | USD15484 |
| Belt conveyor | B500*20m | 1set | USD3220 |
| Belt conveyor | B500*20m | 1set | USD3220 |
| Belt conveyor | B500*20m | 1set | USD3220 |
| Total Amount EXW-Price | USD119415 |

II:SEPECIFICATIONS

Reference of technical data with above machines

| Model | ZSW-960x3800 |  |
| --- | --- | --- |
| Feed chute size(mm) | 960*3800 |  |
| Max.feeding size(mm) | 500 |  |
| Handling capacity(t/h) | 90-200 |  |
| Power(kw) | 11 |  |
| Weight(kg) | 3980 |  |
| Overall Dimension(mm) | 3882*2224*2121 |  |

| Model | PEF600×900 |  |
| --- | --- | --- |
| Power(kw) | 75 |  |
| Max feed size(mm) | 480 |  |
| Adjustment scopes(mm) | 75-200 |  |
| Production capacity(m³/h) | 40-120 |  |
| Rotating speed of main shaft(r/min) | 255 |  |
| Overall dimensions (1×w×h)(mm) | 2792×2168×2250 |  |
| Weight(kg) | 17600 |  |

| Belt Width(mm) | 500 | 650 | 800 |  |
| --- | --- | --- | --- | --- |
| Belt Length (m) /Power (kw) | ≤12/3 | ≤12/4 | ≤6/4 |  |
| Belt Length (m) /Power (kw) | 12∽20/ 4∽5.5 | 12∽20/5.5 | 6∽15/5.5 |  |
| Belt Length (m) /Power (kw) | 20∽30/ 5.5∽7.5 | 20∽30/ 7.5∽11 | 15∽30/ 7.5∽15 |  |
| Belt Speed (m/s) | 1.3∽1.6 | 1.3∽1.6 | 1.3∽1.6 |  |
| Capacity(t/h) | 40∽80 | 131∽323 | 278∽546 |  |

| Model | PF-1214 |  |
| --- | --- | --- |
| Specification(mm) | Φ-1250×1400 |  |
| Feeding opening size(mm) | 400×1430 |  |
| Max.feeding size(mm) | 400 |  |
| Capacity(t/h) | 130-180 |  |
| Power(kw) | 160-200 |  |

| Model | 3YK1860 |  |
| --- | --- | --- |
| Feed chute size(mm) | 3 |  |
| Max.feeding size(mm) | 5-200 |  |
| Handling capacity(t/h) | ≤400 |  |
| Power(kw) | 250-600 |  |
| Weight(kg) | 22 |  |
| Overall Dimension(mm) | 9200 |  |

Ⅲ Commercial Terms

1. Delivery time: 30days after receiving the prepayment.

2. Payment terms:Prepayment: 30% of the total amount to be paid within 5 working days after signing the contract by TT, the 70% of the total amount to be paid by TT after inspection & before delivery.

3. Guarantee: 100% brand new when leaving the factory. we guarantee quality of the machines for a period of one year from the trail run finish(exclude easily damageable parts). But the expense of going abroad of technical engineers should be paid by buyer.

4. Installation: If you require the installation service from us. We will send one technical engineer to your site to guide installation, take trail run and train the workers. Expenses should be paid by the buyer, including the visa, round-trip tickets, insurance, hotel, food and 80 dollars salary per day.

5. Packing: The goods would be processed to be rustproof and moisture proof before delivery. The small parts are packed into wooden box.

6. We will supply foundation drawings after signing contract.                                                                                                                                                                                                                        7. Period of validity: This quotation is available in 60 days since issued.