Quote Sheet for 200m3/h bucket chain gold dredger

Dated: Nov.14, 2012.

Customer’s information

Customer’s name: Mr. GUILLERMO PENFOLD

Company: PENFOLD INTERNATIONAL TRADIG GROUP

Email:

Tel:

Fax：

Qingzhou Haiyang Ore Machinery CO.,Ltd.

Contact:

Mobile:+86-18253616354

Tel: +86-536-7572677

Fax: +86-536-7572877

Website:www.qzhaiyang.en.alibaba.com

www.washajixie.net

Factory Add 1: NO.99, Binhai Economy Development Zone, Weifang City,

Shandong Province, China.

Factory Add 2: NO.77, Huanglou Economy Development Zone,Qingzhou City,

Shandong Province, China.

- Product images for 200m3/h bucket chain gold dredger

- Specifications for 200m3/h bucket chain gold dredger

| Qingzhou Haiyang Ore Machinery Manufacturing Co., Ltd. |
| --- |
| Gold dredger for dredging 20m and working load 200m3/h |
| Item | Specifications | Note |
| Capacity | 200m3/h |
|  | There is 5cubic water in the mixture of 100cubic sand, stones and other things |
| Functions | Sand dredging and gold mining |
| Total hull size | 40*6.5*6.0m | Length*breadth*height |
| Hull size | 32*6.5*1.5 m | Length*breadth*height, |
|  |  | two groups |
| Single pontoon size | 32*2.2*1.5m | Length*breadth*height |
| Steel standard and thickness | CCSB/6mm |  |
| 45°Digging depth | 18m | From water level to the biggest depth |
| Single gold machine power | 11kw |  |
| Hopper volume | 0.14 m³ |  |
| Hopper size | 0.70*0.80*1.0*0.27m | Height*breadth*depth*length |
| Hopper No. | 124 |  |
| Hopper power | 90kw-8 |  |
| Cross power | 4ton/7.5kw*2 | In the water level |
| Lifting power | 10ton/22kw/650Reducer |  |
| Belt chute machine size, power | 4m*1.1m/5.5kw | Length*breadth/power |
| Large particles of gold recovery agitation chute | 2.2kw/1set | Power/set |
| Platform maintenance crane | 5ton |  |
| Model centrifugal machine /power/number | L1000/11kw/2sets |  |
| Total power | 150kw |  |
| Operating system | Electric | Working cabin for operating or controlling |
| Parking generator | 15 kw |  |
| MOQ | 1set |  |
| FOB price | USD212,000 | Generator set excluded |
| Valid date | 2months |  |
| Port | Tianjin |  |
| Leading time | 30days | From the first down payment received |
| Weight | About 74 tones |  |
| 1.1m draught | 80tones | 6tones diesel and 5tones fresh water added |
| Package | In bulk |  |
| Payment | TT |

3. Description about chain bucket sand dredger

It is a kind of non-self-propelled gold dredger, used for sand dredging and gold mining from river, pond, reservoir and shallow water, low cost and easy operating. Because can be dismantle and put into the high container, our engineers and workers will be installing and assemble on the working site, training how to operating and maintaining the dredger at the same time.

Features:

1. Simple, rapid assembly and dismantling

2. Spare parts and floating pipe available

3. Transportable by road, rail or sea

4. Reliable hydraulic system

5. Fresh water engine cooling system

6. Efficient fuel consumption

7. Simple operation

3.Parameter explanation

1.Working capacity:  mixture of sand, water and mud of sand digging in one hour, there is 5% water in 100m3/h capacity.

2. Discharge distance: which refers to the distance from the center of working site, to the destination where you want the sand or mud conveys to.

3. Dredging depth: vertical distance from the water level to the depth where the sand or silt being dredged.

- L*W*H: which means the length, width and height of the chain bucket sand dredger