Feedback form of model selection for customers

Please fill the form in detail so that we can provide you the most suitable model/design.!

Company     CAO TRANSZVUK, UKRAINE             Tel    00380665521599

Add   ____6,STR._NAHIMOVA,ODESSA,UKRAINE,65014,   Fax  +38(048) 728-01-02

1. Raw material    啤酒糟

2. Shape of raw material

□Mushy

3. General characteristics of raw material

Primary moisture of raw material:   89      %

Specific gravity of raw material:          kg/m3

Max bearing temp. of raw material:    达750 ℃

4. Special characteristics of raw material

□Viscosity  高

5. Requirements for drying

Final moisture content of finished product:10-12 %  Product capacity: 当湿度为10%-12%时，7500 kg/h

Finess of finished product:    长达20mm

Drying method: □Continuous drying

6. Required material of machine

□Others:  没有要求

7. Heat source can be supplied

□Steam  □Hot water  □生物燃料炉# 锅炉烟道的气体温度=180C （可以将它们利用起来）

8. Other requirements:  如果干燥采用蒸汽的话-我方有锅炉可以供给干燥用的蒸汽。在干燥酒糟时所得蒸汽我方希望能在生产啤酒的过程中再次利用 。

表1. 新鲜酒糟的养分指标

指标

酿酒厂           "Сан Инбев"  "Степан Разин"  "Балтика"	"Хайнекен"

总湿度, %        81,6          83,4            76,4            78,2

干燥物质, %      18,4          16,6            23,6	        21,8

粗蛋白, %        3,78           4,12           5,63	         4,93

粗纤维, %        3,37           3,24           4,69	         3,98

粗脂肪, %        1,76           1,5            2,13	         1,8