ZHP-670B Single Layer Plastic Sheet Extruder

XJ-2 Mixing Machine              FS-650 Crushing Machine             ZHLS-10 Cooling Tower

| Item | Description of Goods | Quantity | Unit Price (USD) | Amount (USD) |
| --- | --- | --- | --- | --- |
| 1. | ZHP-670B Plastic Sheet Extruder | 1 set | 22000.00 | 22000.00 |
| 2. | XJ-2 Mixing Machine | 1 set | 500.00 | 500.00 |
| 3. | FS-650 Crushing Machine | 1 set | 3000.00 | 3000.00 |
| 4. | ZHLS-10 Cooling Tower | 1 set | 800.00 | 800.00 |
| FOB Ningbo, China TOTAL: | 26300.00 |

Quotations:

TOTAL: SAY FOB NINGBO CHINA U.S. DOLLARS TWENTY SIX THOUSAND THREE HUNDRED ONLY!

FEATURES:

| MODEL | ZHP-670B Single Player Sheet Extruder |
| --- | --- |
| Hard gear, Strong torque, low noise | Full frequency conversion control (Danfoss) |
| Screw material : 38 crMoAL Nitrogen treatment: 0.4 - 0.7mm | Roller Hard chromium plating 0.08-0.18mm Hardness: HRC58-62 Surface roughness: ≥Ra |
| 5 Heating zones of the screw | 3 Heating zones of the die head |
| Motor screen changer system | Energy-saving Die head |
| Individual 45° Three roller control system | CHINA Chint Electric |
| PID Adjusting Memory & Antijam Digital Temp. Control |  |

| MODEL | ZHP-670B Single Player Sheet Extruder |
| --- | --- |
| WIDTH OF DIE HEAD | 700mm |
| MATERIAL | PP.PE |
| WIDTH OF SHEET | 680mm |
| THREE ROLLER SIZE | Ф350*700mm*3 |
| THICKNESS OF SHEET | PP.PE:0.3-2.5mm |
| SCREW SIZE | Ф110 1:32 |
| TOTAL POWER | 110kw |
| WORKING POWER | 65kw |
| SPEED | 15-20m/min |
| CAPACITY | 150kg/h |
| DIMENSION | 12*1.5*2.2m |
| WEIGHT | 5200kg |

Generations:

ZHXS-1200/700 Vacuum Forming Machine

Air Compressor                Egg Tray Sample       ZHLP-30 Hydraulic Punching Machine

Quotations:

| Item | Description of Goods | Quantity | Unit Price (USD) | Amount (USD) |
| --- | --- | --- | --- | --- |
| 1. | ZHXS-1200/700Vacuum Forming Machine | 1 set | 28000.00 | 28000.00 |
| 2. | ZHLP-30 Hydraulic Punching Machine | 1 set | 6000.00 | 6000.00 |
| 3. | Air Compressor | 1 set | 5000.00 | 5000.00 |
| 4. | Mould | 1 set | 3800.00 | 3800.00 |
| FOB Ningbo, China TOTAL: | 42800.00 |

TOTAL: SAY FOB NINGBO CHINA U.S. DOLLARS FORTY TWO THOUSAND EIGHT          HUNDRED ONLY!

Generations of ZHXS-1200/700 Vacuum Forming Machine:

| Suitable Sheet(mm) | PVC PS PET PP | Expansion PSP |
| --- | --- | --- |
|  | Width 500-700 Thickness 0.1-1.2 | Width 500-700 Thickness 1-3.5 |
| Feeding Length (mm) | 600-950 Stepless adjustment |
| Max.MouldingDepth (mm) | Negative mould 200 positive mould 200 |
| Speed (mould/min) | 3-8 times/min |
| Power Supply | AC380/220V 51kw (Max) |
| Air Consumptions | ≧1.5M3/mim(External air supply) |
| Working Pressure | ≧0.6Mpa |
| Dimensions(mm) | 7500×2000×2250 |
| Weight(kg) | 3000 kg |

MODEL:   ZHJY-6B CUP PRINTING MACHINE

| Item | Description of Goods | Quantity | Unit Price (USD) | Amount (USD) |
| --- | --- | --- | --- | --- |
| 1. | ZHJY-6B Cup Printing Machine | 1 set | 60000.00 | 60000.00 |
| FOB Ningbo, China TOTAL: | 60000.00 |

Quotations:

TOTAL: SAY FOB NINGBO CHINA U.S. DOLLARS SIXTY THOUSAND ONLY!

Features:

Well proven color heads, based on decades of manufacturing experience.

Six color heads each provided with eight distribution rollers.

Sharp print results with two form rollers on each color head.

Easy access to product handling areas and print areas.

Optimum product feeding with separate screw feeder motor.

Graphic operation panel for easy machine-control.

Belt feeder with pressure control.

Corona pretreatment with easily adjustable  electrodes.

Quick change mandrel disc assembly.

Mandrel rotation control for all around pretreatment and curing.

High powered ‘Curing on Mandrel’ UV-lamp system with stand-by mode.

Counting & stacking with packing table.

Specification：

| MODEL | ZHJY-6B |
| --- | --- |
| Min./max. Product height: | 30-180mm |
| Min./max. Rim diameter: | 40-140mm |
| Max. Printing height: | 120mm |
| Min./max. Taper: | 0-12° |
| Printing Speed | 5000-12000pcs/hour |
| Total power: | 18kw |
| Weight: | 4 ton |
| Dimension: | 5000*2400*2500mm |