WATERJET TECHNOLOGY CO., LTD

Tel: +86-517- 83717533                     FAX: +86-517-3717-532

Mobile: +86-1385-23-437-31               Website: http://www.xshcn.com

E-mall：sunrisecutting@hotmail.com

3 ejes CUX4002515

Precio: USD45000 FOB SHANGHAI

Plazo de entrega: Podemos arreglar el embarque dentro de  30 días de trabajo después de recibir el depósito de 30%.

Forma de pago: 30% TT como depósito, 70% TT de saldo antes del embarque.

Instalación y capacitación:

Vamos a enviar uno o dos Ingeniero para instalar y para entrenar durante 7 días. Boletos de ida y vuelta de oso de cliente y alojamiento, cobramos US $ 100/día para el ingeniero.

Garantía: Período de garantía de la máquina es de un año desde la fecha de Comisión de la máquina, arreglaremos el reemplazo libre de cualquier pieza defectuosa. Durante el período de garantía, esta garantía no cubre las piezas de desgaste, fallos y también partes consumibles causan debido a funcionamiento por el cliente. Y el cliente debe seguir estrictamente las instrucciones y de nuestro ingeniero y las instrucciones.

Lo siguiente es la especificación:

| ARTÍCULO | DESCRIPCIÓN | CONFIGURACIÓN ESTÁNDAR |
| --- | --- | --- |
|  |  | MARCA | MODELO |
| 1 | SISTEMA UHP | Intensificar UHP | JE STYLE(USA) | CUX400 |
|  |  | Sensor de marcha atrás UHP | CONTRINEX(Suiza) | DW-AS-501-P20 |
| 2 | SISTEMA LP | Motor de 3 fases AC | WNM(China) | Y2-225S-4-B35 |
|  |  | Bomba de desplazamiento | Jing Gong(China) | 63SCY14-1B |
|  |  | Válvula de inversión electro-hidráulico | YUKEN(Japón) | DSHG-04-2N2-T-D24-N1-50 |
|  |  | Eletromagnetic Relief Valve |  | S-BSG-06-2B3B-D24-N1-51 |
| 3 | SISTEMA DE ENFRIAMIENTO | Sistema de enfriamiento por agua | Sunrise(China) |  |
|  |  | Enfriador de panel | Colliers(Taiwan) |  |
| 4 | SISTEMA CNC | Husillo de bolas recirculantes | TBI(Taiwan) | SFUR SERIES |
|  |  | Guía de movimiento lineal |  | BRH SERIES |
| 5 | SISTEMA CNC | Sistema de control | Washing(China) | 320W |
|  |  | Programa Software | CNCKAD(Israel) | V10.306 |
|  |  | Servomotor | Yaskawa(Japón) | SGMGV-30ADC61, SGMGV-09ADC61 |
|  |  | Servodrive |  | SGDV-200A01A, SGDV-7R6A01A |
| 6 | Componente de electrones | PLC | Siemens(Alemania) | S7-200-CN |
|  |  | Interruptor | Schneider(Francia) | 3P C65N C63 |
|  |  | Relé |  | RXMZLB1JD, 24V(DC) |
|  |  | Fusible |  | RT18-32 |
|  |  | Fuente de alimentación |  | ABL1REM24062,24V |
|  |  | Contactor AC |  | LC1-D80M7C,220V (AC) |
|  |  | Controlador de temperatura |  | SW-C4 |
|  |  | Interruptor de proximidad |  | DW-AS-501-P20,NPN |
|  |  | Protección térmica |  | LRD-3359(48-65A) |

Información del banco:

Nombre del banco: BANK OF JIANGSU CO., LTD

Código Swift: BOJSCNBN

Beneficiario: Jiangsu Sunrise Water jet Technology Co., Ltd.

Número de cuenta: 10201488000004557

Dirección: 18# North Feiyao Road Huaian city Jiangsu Province China

: DESCRIPCIÓN TÉCNICA:

La máquina de corte por chorro de agua Sunrise is la máquina de corte por chorro de agua UHP CNC con completar funciones y su forma independiente innovado por nuestro equipo basado en el americano introducido tecnologías avanzadas.

La máquina se incluye las características como lo siguiente:

√ A Bomba de presión alta

√ A Máquina de herramienta CNC

√ A Mesa de corte

√ An Sistema automático de entrega abrasivo

√ A Gabinete del controlador CNC

√ A Cabezal de corte

UHP             Automatic Abrasive             Machine tool

Pump            Delivery System

Cutting head      Cutting Table             Controller Cabinet

| Recorrido de eje X | 2.5M |
| --- | --- |
| Recorrido de eje Y | 1.5M |
| Recorrido de eje Z | 0-150mm |
| Tipo de máquina | Tipo voladiza |
| Espesor máximo de material | 120mm-150mm |
| Precisión de control | ±0.002mm |
| Precisión de corte | ±0.1mm |
| Presión de trabajo máxima | 60000 psi (400Mpa) |
| Potencia de motor | 22kw/30kw |
| Tipo de bomba con presión alta | Tipo de intensificado,30 HP (mínima) |
| Potencia | 380 Volt / 3 fases / 50 Hz |

* Fuente de alimentación para el sistema y su gabinete de controlador, puede ser fabricado cumplir cliente necesita, mientras 3 fases

THE HIGH PRESSURE PUMP :

The High Pressure pump is the core power of the water jet machine. It is the heart of the whole machine, it pressurizes the water which has been filtered to 300Mpa-400Mpa (45000psi-60000psi), then form about triple velocity of sound water jet when pass the orifice. It changes pressure energy into the concentrated kinetic energy to achieve the goal of cutting any materials.

√Adopt technology and parts of America (such as high pressure cylinder, plunger, seals and so on），prolong the using life, upgrade cutting precision （one of the advantages of our product）。

√Adopt technology and parts of America (such as high pressure cylinder, plunger, seals and so on），prolong the using life, upgrade cutting precision （one of the advantages of our product）。

UHP intensifier                       Pump

√ Imported reversing sensor，reversing become more placidity and credibility (one of the advantages of our product)Solve the problem such as actuator stem broken, oil leakage from seal, collar cap of the end of actuator stem become flexible and other defect cause by typical exchange sensor, with steady and credibility exchange, safety, wear well, as for this part the cost is higher than other producer, so it can bring higher efficiency for the client.

√ Double protection system by high pressure and low pressure, automatic power off system, make sure operation safety.

THE CNC MACHINE TOOL

√ Adopt cantilever structure. X、Y axis boll screw via elasticity coupling connect with motor directly, reduce libration, transmission precision more higher.

√ Load and unload work piece from three directions. It solve the problem in overpass machine which can only load and unload the material from two side and limit the dimension of the material. It can put larger work piece in bed of cantilever machine which can larger than the bed of the machine. During the process of running , it will not have the problem which two boll screw is out-of –step , and it will not owning to the unbalanced pressure on synchro strop which will cause breakage of machine so that it can’t insure the precision of cutting.

√ Adopt high grade servo drive system，ball screw and guidway is also adopt international brand. X axis adopt the boll screw which diameter is 50mm, ensure the whole machine can transmission steady

√ Select high grade dustproof equipment。The life of dustproof equipment we select is more the three times than ordinary ones.

√ Adopt the design that bed of the machine is separate with the cutting flat.

It will not effect by shack when cutting, increase the precision of cutting.

CUTTING TABLE:

√ The machine tool is designed to be separated from the cutting table, so the cutting process is vibration free and can get higher cutting precision.

√ All grizzly bars of the cutting table is insert style, so it is easy to change if one of the grizzly bar is broken.

AUTOMATIC ABRASIVE DELIVERY SYSTEM:

√  Alleviate load of machine beam greatly.

√ High delicacy inductor and signal lamp can clew operator when will add the abrasive to the tank.

√ Big capacity abrasive tank can offer the abrasive for cutting for about 500 to 800 minutes continually. No need add abrasive frequency.

√ Operation is simple, running credibility, no need for maintenance.

√ Automatic Abrasive Delivery System is a part of the whole machine but other company is the select part for buy.

CNC CONTROLLER CABINET:

√  high light 8LCD display.

√  Federate can achieve adjustment of magnification at any time.

√ Adopt PLC control of SIEMENS，which have higher reliability, stronger anti-jamming, more simple maintenance.

√  Via COM、USB interface and PC or U disk for interface directly.

√ Hand-hold machine tool controller is used for control the remove of axis X,

Y, Z took to the machine side by operator.

CAM SOFTWARE:

√  It can be compatible with many format of drawing design software in international，such as ASC、IGS、DXF、DWG、STL、NFL、PRT、STEP and so on.

√ It has the function of automatic radius compensation of cutter.

√ Automatically entering lead-in line.

√ Automatic calculates the length of cut line.

√ Automatic Nesting

AUTOMATIC NESTING INTERFACE

CUTTING SAMPLE:

Metal

Glass

Marble                                       PVC