# Hose crimping machine KM-91H

☆ Advantages:

1. Quick change tool (optional).

- Two option of control modes: normal and computer(optional).

- There is the lubrication and           dustproof system.

- With moving holder.

◇We are able to offer you special equipment which meet your expectations and improve your comfort and efficiency.

◇Our principle: it bases on technology, innovation and service to large the market.

☆ Technical data:

| Crimp range | 1/8" ~1 1/4" 4SP |
| --- | --- |
| Standard voltage & motor | 380V/4kw,220V/2.2KW |
| Opening without dies | 122mm |
| Opening | ±28mm |
| Swaging force | 530T |
| Open | 1.5s |
| Close | 8s |
| Optional voltage&motor | as customer’s requirement |
| No. of standard die set | 10sets |
| Systematic pressure | 31.5Mpa |
| L*W*H | 690mm*465mm*728mm |

- Special:

- NEW foam inserts introduced to protect your machine

from debris dropping into the bottom of the head. With

there you will minimize the risk of debris getting into

the cylinder which could cause damage to seals and

other moving parts of the head. This will significantly extend the life of hydraulic hose crimping machine.

2. The machine head connect by bolts

Result: NO leakage and damage.

☆Die chat:

| Die bore(D) | Die length(L) |
| --- | --- |
| 15mm | 65mm |
| 18mm | 65mm |
| 21mm | 65mm |
| 24mm | 65mm |
| 27mm | 65mm |
| 33mm | 65mm |
| 39mm | 65mm |
| 45mm | 78mm |
| 48mm | 78mm |