# 3000GPD RO system and price

| Item | Product | Model | quantity |  | Remark |
| --- | --- | --- | --- | --- | --- |
| Pre-filter system |
| 1 | Booster pump | CHL2-40（50Hz） （220V/50Hz） | 1 PCS |  | Hangzhou Nanfang Special Pump Q=1.0m3,H=34m,P=0.55kw |
| 2 | Auto multi-sand filter | 12*52 | 1 PCS |  | FRP |
| Specification | Sand | 0.5-1.2mm | 100kg |  |  |
|  | Auto control valve | Fleck 5600 | 1 PC |  | Made in American |
| 3 | Auto Active carbon filter | 12*52 | 1 PC |  | FRP |
| Specification | Carbon | 10-20 item | 25kg |  |  |
|  | Auto control valve | Fleck 5600 | 1 PC |  | Made in American |
| 4 | Auto softeren | 12*52 | 1 SETS |  | FRP |
| Specification | Cation resin | 001*7 | 50 L |  |  |
|  | Salt tank | MC-64L | 1 PC |  | PE |
|  | Auto control valve | Fleck 5600 | 1 PC |  | Made in American |
| RO system |
| 5 | RO system | 0.5m3/h | 1 SET |  |  |
| Specification | Cartridge Filter | 5μPP*20“PP filter 1nos. | 1 PC |  | Blue bottle |
|  | High pressure pump | CDL2-13（50Hz） （220V/50Hz） | 1 PC |  | Hangzhou Nanfang Special Pump Q=1.2m3,H=114m,P=1.5kw |
|  | RO Membrane | LP--4040 | 2 PCS |  |  |
|  | Membrane housing | 4040 | 2 PCS |  | SUS304 |
|  | low Pressure control device | JC-206 | 1 PCS |  |  |
|  | Flow meter | 5 GPM | 2 PCS |  |  |
|  | Conductivity measuring cell | CM-230 | 1 PC |  |  |
|  | Electric Control system |  | 1 SET |  | Import electric parts |
|  | Piping connection | UPVC | 1 SET |  |  |
| 6 | Frame | 1400*550*1600mm 700*550*1600mm | 1 SET |  | SS. |

Technical Parameter

1.Feed water:

  - Feed water flow: 1.0-1.5m3/h

  - Qualification for feed water to the membranes :

- highest water turbidity : 1 NTU

- highest chlorine content: 0.1mg/l

- highest silt density index  (15mins): 5

- TDS:  ≤350PPm

- PH scope:  3-10

- Temp. scope:  5-40℃

The membranes will meet damages in case of feed water under the above qualification. And the membranes will not work at their best.

2.Power supply

AC220V/ 50Hz

3.outlet pure water quality:

  - water flow :0.5m3/h @25℃

  - Desalinization rate ：≥98% @25℃

3.3 Recovery ：50~60%