ZRY-450A AUTOMATIC UV FLEXOGRAPHIC PRINTING MACHINE

A. Characteristics:

- Adopt the ceramic anilox cylinder to transfer the ink.

- Unwinding and rewinding are controlled by magnetic power brake, clutch, (Or controlled by auto tension controller of Mitsubishi of Japan).

- Each printing unit adopts 3600 plate-adjustment.

- IR dryer for each printing unit. (UV dryer is for option)

- This machine has die-cutting station, and it can make printing and die cutting finished in one process.

- The ink rollers will be separated from the printing roller, and keep running when the machine stopped.

- The machine can finish material-feeding, printing, lighting, drying, laminating, die-cutting and rewinding in a lump. It is an ideal machine for printing note and top-grade adhesive label.

①IR Dryer
   UV curing system
②Turn bar 
③Tension control system(Mitsubishi of    Japan) 
④Joint Web-guiding
⑤Laminate device 
⑥Waste wind-up device 
⑦Rotary Die-cut device 
⑧Wind-up tension control 
⑨Air shaft 
⑩Adjusting handle for left/right 
⑾360 registration device 
⑿Flexo print unit
Note: The list which with ※ is the          optional device

B. Main Technical parameters:

| MODEL | RY-A450 |
| --- | --- |
| Printing speed | 60m/min |
| Printing color | 6colours |
| Max. width of paper | 450mm |
| Max .printing width | 440mm |
| Max. unwinding diameter | 600mm |
| Max. rewinding diameter | 550mm |
| Printing length | 175-320mm |
| Precision of chromatography | ±0.1mm |
| Dimensions | 2.25mX1.5m X2.6m |
| Machine weight | About 2500kg |

C. Configuration

The chosen electric apparatus for the machine:

- Electric apparatus: Made by CHINT group;

- Temperature controller: Made in Shanghai.

3.  Web guide system

Summarization:

A. Unwinding unit

B. Printing color system

C. Rewinding unit

A. Unwinding unit

- Unwinding diameter: φ600㎜.

- Unwinding shaft: 3 inches φ76mm air shaft,

- Tension control: magnetic powder arrester.

- Controller: 40MTA  pressure sensor from  Mitsubishi of Japan

B. Color system

- Printing cylinder: 55teeth-120teeth ( printing length:175mm-380mm)

- Pneumatic press roller;

- Transitional idler pulley: φ67mm aluminum alloy rollers;

- Color registering system: manual registering system.

- Drying system: UV

- Printing main motor: AC frequency conversion motor.

C. Rewinding unit

- Rewinding diameter:φ550mm

- Rewinding shaft: 3 inchesφ76mm air shaft.

- Automatic control rewinding: magnetic powder clutch, 40MTA pressure sensor (made in Zhejiang).

D. Main Equipments:

|  | Description | Main technology | Supplier | Remark |
| --- | --- | --- | --- | --- |
| Machine power | Main machine | 2.2kw 380V | Lichao,Shanghai |  |
|  | Heating | 2.1w x 6 groups | Guangzhou | 6 group |
|  | Ink roller motor | 25w x 6 groups | Chenggang, Taiwan | 6 group |
|  | Total power | 8kw |  |  |
|  | Unwinding | Press sensing inspection，automatic tension control | Pressure sensor:： Tension controller: ZX brand: Magnetic Powder arrester: | 〈LE-40MTA-E Torque：50N/M |
|  | Unwind traction | Automatic tension control | Tension controller: Made in Wenzhou | Torque：25N/M |
|  | Color group | Oven constant temperature controlled by temperature controller,. the more reasonable glue distributing can be reached by the delayed controlling of the ink roller and the anilox roller. |  |  |
|  | Rewinding | Press sensing inspection，automatic tension control | Pressure sensor:：Made in China Tension controller: Made in China Magnetic Powder arrester: Made in China | 〈LE-40MTA-E〉 Torque：50N/M |
|  | Main machine | Frequency conversion control | Transducer: Inovance | Stop machine without material and stop machine when finished the printing length (measured by the meter-counting) controlled by Miscomputer. |
|  | UV |  | 1 SET |  |