雁 峰 集 团 有 限 公 司

YANFENG  GROUP  CO.,  LTD

ADD: PINGYANG ECONOMIC DEVELOPMENT ZONE, ZHEJIANG, CHINA

E-MAIL: kathy@yanfeng.cn                   WEBSITE: www.yanfeng.cn

TEL: 13757881656                            FAX: 0086-57763032888

BRIEF INTRODUCTION OF CIRCULAR LOOM

As a manufacturer producing circular looms with the most various series and the most complete specifications, our factory has produced different circular looms with fourteen models in twelve series which can satisfy the woven bag production with the layflat width from 200mm up to 2100mm.

Small-sized Four-/Six-shuttle Circular Loom and Four-shuttle Circular Loom can weave all sorts of small-specified woven sacks; Medium-sized and Big-sized Six-shuttle Circular Loom and Eight-shuttle Circular Loom can weave various flexible intermediate bulk container(FIBC) bag, tarpaulin for rainproof and sunshade as well as woven geofabric; High-speed Circular Loom for Mesh Bag can be used to weave mesh bags for packaging vegetables, fruits and melons.

With a twenty-five year history and abundant experience in producing circular looms, our factory continues developing new products and twenty items have been granted with National patents. Meanwhile, we pursue to improve our old products in order to make them much more perfect.

Featured with high rotational speed, low noise, economic power consumption and convenient operation and maintenance, our circular looms can even use the yarn made by recycled materials.

Price list of woven bag making plant

Description                  Type         Unit price          Qty.        Amount

1 High-speed flat yarn extrusion line YF-SPL-120/30/1500            1set       $234560

2. Big six shuttle circular loom YF-YZJ-6/2100     $29800           6set       $178800

3. Granulator                  SJ-FL_120-2            $6500                 1set           $6500

4. Narrow fabric loom        CDB-100*2        $8700           1set        $8700

5. Big cutting machine         CD-III           $2900           2set        $5800

6. Big sewing machine         GB4-1           $600           20sets      $12000

7. Tape winding bobbin      38x230mm (dxl)     $0.32/pcs           40000pcs    $12800

8. Spare parts                                   $10000             a lot       $10000

Total                                                                           $469100

The above price is based on FOB Wenzhou port china including installation charge.

FLOW CHART OF WOVEN BAG PRODUCTION

1.PP.HDPE material ----------high speed flat yarn extrusion line------------ 5.circular loom-------8.bag cutting   machine--------9.sewing machine-----10.baling press

Flat yarn extruder YF-SPL-110/30/1200

THIS MACHINE, USING MATERIAL OF PP & HDPE, THROUGH HEATING, EXTRUDING AND DRAWING, MAKES TAPE THAT IS THEN WINDED FOR THE WEAVING OF THE CICULAR LOOM.

HAVING BEEN IMPROVED SO MANY TIMES, THE MACHINE CAN USE 100% RECYCLED PP/PE GRANULES OR POWDER TO PRODUCE YARN. THE SCREW AND CYLINDER ARE MADE OF NITRIDED 38CRMOA1A ALLOY STEEL, THE HARDNESS OF WHICH CAN REACH OVER HV950. HELICAL GEAR REDUCER MADE OF 20CRMNTI ALLOY STEEL IS APPLIED TO THE EXTRUDER AS WELL. THE CHAIN WHEEL ADOPTS 45# MEDIUM CARBON STEEL AFTER BEING TREATER BY HIGH-FREQUENCY QUENCH. THE DRIVING ROLLERS ARE ELECTROPLATED WITH HARD CR AND THE SELF-CONTROL TENSION WINDING ROLLER IS ADOPTED BY THE TRACTION UNIT. MOREOVER, THE BARREL, TEE FITTING AND DIE ADOPTS ALUMINIUM CAST HEATER WHICH IS DURABLE.

MAIN TECHNICAL SPECIFICATIONS:

Max. Extrusion output: 380kg/h

Screw dia: 110mm

L/D ratio: 30:1

Rotational speed of screw: 20-120rpm

Width of die lip: 1200mm

Max. linear speed: 280m/min

Flat yarn denier: 60-200tex

Drawing ratio: 4-10

Number of winder spindles: 208

Size of bobbin: 38 * 230mm

Installed power: 320kw

Normal power consumption: 170kw

Installing dimension: 34000 *3800*3200mm

Weight: 30000kg

Single spindle winding machine S-SDC-208A

THIS MACHINE, WITH 2.2-3KW MAIN MOTOR ONLY, IS OUR ENERGY-ECONOMY INVENTION. IT ADOPTS CARDIOID CAM TO REPLACE THE FORMER RECIPORCATION-SHAFT MECHANISM OF COMBINATION WINDING MACHINE. ITS GUIDING AXLE ADOPTS GCR15 BEARING STEEL AND THE GUIDING PUSHING-BOARD IS MOVED BY THE MATCH BETWEEN LINEAR ROLLING BEARING AND GUIDING AXLE. IN THIS WAY, WITH ROLLING FRICTION FOR THE RECIPROCATING MOVEMENT, THE MACHINE CAN ACHIEVE LESS ABRASION, STABLE MOVEMENT AND FLAT WINDING SPINDLE. ITS OVERALL LENGTH IS GREATLY SHORTENED BY ADOPTING 5 LAYERS ON BOTH SIDES, WHICH IS GOOD FOR MATCHING WITH PLASTIC TAPE DRAWING MACHINE.

MAIN TECHNICAL SPECIFICATIONS:

MODEL                            S-SDC-256A

LAYER NUMBER OF SPINDLE           4

NO. OF SPINDLE                      256

DIMENSION OF BOBBIN (OD×L)       38×230MM

SPEED OF TAPE WINDING         50-280M/MIN

POWER TOTAL                        48KW

INSTALLING DIMENSIONS(L×W×H) 15500×3200×2000MM

WEIGHT                             9200KG

RECYCLING GRANULATOR SJ-FL120-II

THIS ASSEMBLY CAN BE USED TO PROCESS CLEAN OR OLD BROKEN PP/PE PLASTICS INTO GRANULES THAT CAN BE RE-USED AS THE RAW MATERIALS. THE SCREW AND CYLINDER ARE MADE OF 38CRMOALA ALLOY STEEL AFTER BEING NITRIDED, WHICH IS DURABLE.

IT CONSISTS OF MAIN EXTRUDER AND SUB-EXTRUDER, WATER TANK AND CUTTING PART WITH ALLOY ROTARY CUTTER. BESIDES, IT IS OPTIONAL TO BE COLLOCATED WITH DRYING FAN.

MAIN TECHNICAL SPECIFICATIONS:

MODEL                                 SJ-FL120-II

DIAMETER OF SCREW                     120MM

L/D RATIO OF MAIN-SCREW                 10:1

L/D RATIO OF SUB-SCREW                  6:1

POWER OF MAIN MOTOR                  18.5KW

POWER OF SUB-MOTOR                  7.5KW

ROTATIONAL SPEED OF SCREW        50-80R.P.M

GROSS HEATING POWER                 12KW

PRODUCTION CAPACITY                40-80KG/H

POWER OF CUTTING                      1.1KW

HEATING POWER                         12KW

INSTALLING DIMENSIONS(L×W×H)  4500×2000×1100MM

WEIGHT                                  1200KG

Big-sized six-shuttle circular loom

Big-size six shuttle circular loom is used to produce flexible intermediate bulk container (FIBC) bag, woven geo-fabric, while the eight-shuttle circular loom can make tarpaulin for rainproof and sunshade.

With frequency-conversion step-less speed regulation, it is configured with warp/weft breaking detecting system, warp/weft ending monitoring system as well as automatic meter-counter

YF-YZJ-6/2100:

Shuttle: 6

Lay-flat width (mm): 1400-2100

Max. Warp(pcs):2400

Revolving speed of mainframe(r/min):35-70

Gross power of motor (kw):10/15

Capacity (m/h)(40wefts/100mm):30-60

Narrow fabric loom

Number of narrow fabric (pcs): 2

Width of narrow fabric (mm): smaller than 100

Width of weft (pcs/inch): 7-10pcs/inch

Weight (kg):800kg

Power if main motor（kw）: 1.5kw

Installing dimensions (L*W*H) (mm): 7000*1800*2100

Sewing machineGB4-1

Max. Sewing speed(r/min):1400r/min

Thread chain type chain (mm): double thread

Length of thread: 9-14mm

Max. Sewing thickness (mm):14mm

Power of motor (kw):0.55kw

Applied range: container sack

Cutting machine

CD-III: max width of cloth roller (mm):2100mm

Weight of cloth roller (kg): smaller than 1000

Power of thermal cutting (kw):15

Power of motor (kw):1.5

Installing dimensions (L*W*H):7000*2500*1500

Weight: 600kg