Busbar multi-function processing machine

Model: BM503-S

Part 1:Main features :

- In the bending unit, bending angle NC controlled ( combined control of PLC, grating and touch screen), which is of good precision and easy to operate.

2.  For punching unit, it is very convenient to withdraw& change toolings.

3.  The cutting unit adopts punching shear method, the verticality of the end surface is guaranteed, no deformation of workpiece and the end surface is bright and good appearance.

- The machine uses two work tables and really achieve simultaneous work of the three work stations and avoids the interference of each other.

- The machine is equipped with automatic oil filling and releasing system, which is easy to operate and has cooling functions.

Part 2:Main parameters

| Work table dimension(mm) | Machine weight(kg) | Motor QTY | Total Motor Power(KW) | Work voltage | Hydraulic Station QTY*SPEC.(Mpa) |
| --- | --- | --- | --- | --- | --- |
| 1PstP:1500*1200 2PndP:840*370 | 1500 | 3+1 | 11.47 | 380V | 3*31.5 |
| Control method: PLC+ Bending angle NC control |
| Punching unit |
| Item | Unit | Material | Thickness(mm) | Max. Diameter of Punching hole |
| Punching capacity | mm | Copper/Aluminum | 15/15 | 25mm |
| Max. Punching Force | KN | 500 |
| Cylinder stroke | mm | 50 |
| Cutting unit |
| Item | Unit | Material | Max. Thickness(mm) | Max. Width |
| Cutting capacity | mm | Copper/Aluminum | 15/15 | 160/160 |
| Max. cutting Force | KN | 500 |
| Cylinder stroke | mm | 50 |
| Bending unit (Bending angle NC control) |
| Item | Unit | Material | Max. Thickness(mm) | Max. Width | Bending accuracy |
| Bending capacity | mm | Copper/Aluminum | 15/15 | 160/160 | +/- 0.5º |
| Max. bending Force | KN | 350 |
| Cylinder stroke | mm | 240 |
| The max. processing dimension when doing vertical bending: width*thickness=100mm*10mm |

Part 3: General description of each work unit

Punch Unit
Fast change of die is realized without any requirement on tool, and the machine can finish round hole punch, oblong hole punch, double hole punch, embossing, copper bar press and copper bar shear etc.

Shear Unit

Two kinds of shearing method for your choice.-punching shear and single shearing.

For punching shear the verticality of the end surface is guaranteed, no deformation of workpiece and the end surface is bright and good appearance. But it wastes the raw material a little.

For single shear, there is a little bevel angle on the work piece but it wastes no raw material.

Bend Unit

Plain (horizontal) bending, vertical bending ,elbow pipe bending, connecting terminal and copper busbar bending etc can be carried out via changing of die. The die is simple and easy to change.

Part 4: Accompanying standard toolings:

- Punching

Round and oblong holes total 8 sets, size as per customer’s requirement

- Vertical bending 1 set

- Horizontal bending 1 set

- Embossing 1 set

- Cutting  1 set

Note: The connecting terminal die is not included in the standard tooling, if it is needed, pls inform us cable sizes.

WORK PIECE EXAMPLES