Axial clearance:0.05-0.10mm

Static load ratings:Coa=470kn

Modul M=3

Number of teeth:Z=59

Addendum coefficient :X=0

Accuracy class:998GJ-GB10095

2-M8*1 Equally spaced  Threaded Depth 10

20-Ф11 holes Equally spaced

Taper pin hole Ф8 Drilled with plug

Note:

- Material tempered and quenched hardness:HB229-269

- Raceway case harder hardness:HRC55-60  at hardness gap on outer race on which less than 30mm

- Ball and separator alternat placed

- Grease :Alvania EP2 or Equivalent

- Rubber seal must be installed with permaband or equivalent ,clean seal groove thoroughly with alcohol before installation.