Quotation

We supply YT Series Flexographic Printing Machine, the newest information and quotations as follow:

Ⅰ.Feature:

1. Easy operation, flexible starting, accurate color register .

2.The meter counter can set printing quantity according to the requirements, stop the machine automatically at the quantity or when the material is cut off.

3.Pneumatic printing cylinder lift and lower, it will stir the printing ink automatically after lifting.

4.The printing ink is spread by the anilox cylinder with even ink color.

5.Reliable drying system coordinated with high-speed rotation, it will automatically break circuit when the machine stops.360continuous and adjustable longitudinal register device.

6.The frequency control of motor speed adapts to different printing speeds.

7. Suitable for printing the packing material as PE and PP plastic bags, glass papers rolling papers, etc.

Ⅱ. Parámetro Técnico Principal

| Modelo | YT-6600 |
| --- | --- |
| Anchura de Entrada de Impresión | 600mm |
| Ancho de impresión | 560mm |
| Longitud del producción de impresión | 191-990mm |
| Diámetro del material de rollo | φ450mm |
| Velocidad de impresión | 5-80m/min |
| Espesor de la plancha de impresión | 2.3mm |
| Potencia total | 10.87kw |
| Dimensión total | 6800×1600×2400mm |
| Peso | 3500kg |

Detail specifications:

1. Unwinding parts

1) roller length: 800mm

2) effective printing roller length: 600mm

3) roller core diameter: 76mm

4) max. unwinding diameter: 800mm

5) unwinding type: mechanical

2. Traction parts

1) traction composed: roller, chrome plate roller

2) group count: 6groups

3. Printing parts

1) printing composed: chrome plate roller, printing plate roller, cob-webbing roller, rubber roller

2) plate roller perimeter: 100-350mm

3) printing plate material: resin or rubber

4) drive pattern: bevel wheel drive

5) printing topping: 360 degree rotate

6) adjustable type: by hand

7)  rise and fall plate adjust: by hand

4. Heating and drying parts

1) heating pattern: first blower then heating

2) heating range: 6colors 6pc

3) heating power: 600mm model: 1.1kw

4) auxiliary heating length: 600mm

5) fan: 2 sets

6) fan power: 600mm model: 2×0.25kw

5. Motor parts

Main motor: 6colors 600 mm : 1.5kw

Transport ink motor: 0.25kw

6. Rewinding parts:

1) roller length: 800mm

2) effective roller length: 600mm

3) roller core diameter: 76mm

4) max. rewinding diameter: 800mm

5) rewinding pattern: mechanical

7. Main device list:

1. main motor( frequency conversion motor): 1 set 1.5kw ( LiBiao, Shanghai)

2. transport in motor: 1 set 0.25kw ( Libiao, Shanghai)

3. Main frequency converter: 1 set ( Nengli, Hongkong)

4. Fan: 2 sets 2×0.25kw ( Fengyang, Shanghai)

##### 5. Aluminum running roller: Oxidation the surface, staticanddynamicequilibrium

Treatment

6) metal cob webbing roller: 1 pcs per color

7) rubber roller: 1 pcs per color

8) low-voltage apparatus: (China Zhengtai Group)

9) photo electricity correct : 1 set ( made by ourselves)

10) switch: SCHNEIDER, France

11) electrical control box: 1 set ( made by ourselves)

12) Main frame: 1 unit ( made by ourselves)

13) Completely machine casting: Chuangxin casting corp., Henan)

8. Spare component for present:

A tool box include: 1-10 scripts screwdriver; 1 pcs oil gun; 1 set socket head wrench; 2pcs electric switch; 1pcs cocontactor; 2 pcs tubular electric heating element; 1 part of instruction; 1 part of frequency converter instruction)

9. Optional devices

Error-correcting device                                 650 USD / Set

Full automatic Magnetic tension controller                  1500 USD / Set

Digital corona treatment                  600 USD / Set(Depends on the width)

Air shaft                                             160 USD / Set

Ceramic Anliox roll:                                   1600USD/Set

Doctor blade:                                         200USD/Set

10. Ink: This flexographic printing machine support water base ink.

Ⅲ. Cotización  (F.O.B Precio Ningbo puerto)

| Modelo | Precio |
| --- | --- |
| YT-6600 | 12500USD（6colores） |

El período válido de precios tiene una duración de 2 meses.

Ⅳ.Entrega

Dentro de 25 días del envío de la máquina, fabricamos la máquina después de recibir 30% de depósito.

Pago: 100% T/T

Período de Garantía :1 año (odo el dispositivo principal se puede cambiar gratuito dentro de 1 año)

Embalaje: con película estirable y película de la burbuja.

También se puede embalar con la caja de madera (hay que pagar el honorario adicional)