Quotation

Name:  JMQ-320Y Rotary Die Cutting and Slitting Machine

Specifications: Please see list below.

FOB Price: USD 7400

Destination: Port Ningbo, China

(Please be noted that the exchange rate of USD/RMB is finally decided when the date contract comes into effect)

Delivery Time: within 30 working days after we receive the deposit

Payment Term: 100% T/T, 30% T/T in advance as a deposit and the balance before we send the machine from our mill.

Installation: the seller will send for a engineer for installation if customer need. The charge of accommodation, food and round air-tickets, salary USD60 per day for engineer should be paid by the buyer. The normal period of installation is within 7 days, the buyer needs to delay unless special condition.

(Noted: Machine can be shipped after Inspection only.)

Warranty Time:  1 year

Packing: wooden case

Specification:

Name: JMQ-320Y Rotary Die Cutting and Slitting Machine

Technical parameters:

  - Die-cutting material: paper adhesive, polyester film, label

  - Die-cutting width: 320mm

  - Die-cutting length: 177-380mm

  - Die-cutting speed: 70m/min

  - Slitting Speed: 75m/min

  - Positioning accuracy: ±0.1mm

  - Unwinding diameter: ￠500mm

  - Winding diameter: ￠480mm

  - Power of main engine: 2.2kw

  - Total power: 4kw

  - Mechanical structure: Iron and steel

  - Supply voltage: 220v

  - Weight of machine: 600kg

  - Size: (L)1600x(W)900x(H)1300

Configuration：

Main control system: this machine is controlled digital screen. It has multi-functions as edge detection and target detection.

Main motor: adopt Single-phase AC 2.2KW variable frequency to control

Cutting system: Adopted with magnetic powder clutch and magnetic powder brake to control the cutting knife and cutting synchronization.

Motor: adopt Mitsubishi.

Waste collection: Independent motor control

Low-voltage electrical and pneumatic components: Schneider

Rectification: Analog optical eye and control (Kontec)

Frequency converter：Inovance converter