Tel:0086-577-65570088     Fax: 0086-577-65570088  Email: anny@sinceremachine.com

Add: Jiangnan Industrial Area  Feiyun Town  Ruian City  Zhejiang Province  China

Quotation

ZB-G16 TYPE PAPER CUP SHAPER

| Quantity | 1 set |
| --- | --- |
| Pic |  |
| Description | ZB-G16 type high speed machine can make both single and double PE coated paper cups. And also can run the whole procedure of paper-feeding, gluing, oiling, bottom-punching heating, rolling, rimming, rounding, and tripping. Produce coffee cups , ice cream cup and other drink cups . |
| Item | ZB-G16 |
| Speed | 65-75 pcs/min |
| Paper Cup Size | 4-16 ounce or customize |
| Raw material | 150-350g |
| Electricity | 220V50Hz1phase、 380V50Hz3phase |
| Power | 12Kw |
| Net weight | 2800Kg |
| Dimension | 2600×2000×1700mm |
| Price | FOB ningbo 19000USD/ SET |

After-sale service:

A guide book is included to assist with the installation and machine adjustment process and help solve any problems that may be encountered.

1. The ZB-G16 high speed paper cup forming is adjusted one week prior to delivery to make sure our SINCERE machine is in perfect condition.

2. Technicians are available to guide the installation and adjust the machine at the buyer’s factory. this service would be at the buyers expense and include the technician’s salary ,transportation , accommodations, consultation ,etc. as well as $100 USD per diem for the technician .

3. Free training is available and ongoing for the buyer until he fully understands the operation of our SINCERE high speed paper cup forming machine. the buyer would be responsible for airfare and accommodations expenses.

4. SINCERE provides the consumable spare parts at no cost for one year.

Warranty:

- SINCERE high speed paper cup forming machine offers a one year warranty from the shipment date.

- The SINCERE warranty is not applicable to parts requiring normal replacement.

- SINCERE is not responsible for any damage caused by misuse, improper handling, negligent maintenance, intentional injury or other damages.