YN8100 skid steer loader

- Chinese Deutz diesel engine

- Germany Rexroth brand pump

- Japanese double speed motor

- Hydraulic control system

- Luxury close cabin

- Hydraulic brake

- Hydraulic self-leveling system

- High flow output

- Bobcat type quick coupler

| Item | description | Item | description |
| --- | --- | --- | --- |
| Rated operating capacity(kg) | 1500 | Hinge pin height (mm) | 3150 |
| Tipping load (kg) | 3000 | Total height (mm) | 2160 |
| Bucket capacity(m3) | 0.55 | Length with bucket (mm) | 3580 |
| Hydraulic pump flow (L/min) | 100/140 | Length without bucket(mm) | 2880 |
| Engine power (hp) | 100 | Width with bucket (mm) | 2030 |
| Weight(kg) | 4280 | Track width (mm) | 320 |
| Max travel speed (km/h) | 12/16 | Length of track on ground | 1500 |
| Grade ability | 20 | Fuel/hyd oil capacity (L) | 90/90 |

FOB Qingdao : $ 42000.

Packing: 2 units/20' container

4 units/40' container

Optional:

Dongfeng Cummins: + $1200.

Air conditioner:      +$750.

Payment Terms: 20% as down payment, balance before container packing.

Delivery time: 20 days

Guarantee: 1 Year

Our certificate:

We are in Bauma 2013 Germany: