ZS High Efficient Sifting Machine

Main Uses

The machines are applicable to grade of dry powder granules materials in pharmaceutics, chemical industry, foodstuff industry, etc.

Characteristics

The machine consists of the vertical vibrating motor, a sieve bottom, a mesh frame, screening room, the rubber vibrating bowl. This machine can be used for single layer or multiple layers grading.

Advantage

Compact structure, convenient operations and maintenances, stable running, low noise, large quantities of materials-treating, good fineness, strong applicability, etc.

Technical Data

| Model | 400 | 600 | 800 | 1000 | 1500 |
| --- | --- | --- | --- | --- | --- |
| Prouction capacity | 50-300 | 100-800 | 200-1500 | 500-2500 | 1000-8000 |
| Meshes screen | 2-200(mesh) |
| Vibration frequencyed | 1500(times/min) |
| Motor power | 0.2kw | 0.55kw | 0.75kw | 1.1kw | 2.2kw |
| Overall dimension | 405× 800× 1100 | 605× 950× 1150 | 805× 1200× 1150 | 1050× 1350× 1150 | 1950× 1600× 1400 |
| Weight | 200kg | 250kg | 300kg | 380kg | 680kg |

Photo: