Quotation

We supply DYRW Series Stretch Film & Cling Film Slitting and Rewinding Machine, this is the newest information and quotations:

Ⅰ.Feature:

1. It is the latest style of stretch film rewinder in China. It is full automatically rewinding and cutting.

2. Adopt PLC touch screen. Guarantee the operation more correction and easy.

3. The speed is controlled system is: AC motor + Inverter

4. The conveyer belt is the Teflong brand which import from Germany. It is very strong.

Ⅱ.Application

1. It is a kind of multi-functional machine integrated with slitting and rewinding.

2. It mainly slits large-sized or big roller stretch film into small ones, which avoids the split-level film and improves the technical index of product, such as level and appearance quality etc.

Ⅲ. Main Technical Parameter

| Type | DYRW-500 |
| --- | --- |
| Width of finished products | 500mm |
| Power of motor | 1.5kw |
| Linear speed of machinery | 400m/min |
| Roll laying mode | By hand |
| Diameter of parent roll(max) | φ400mm |
| Width of parent roll(max) | 500mm |
| Core specification of parent roll | 3" |
| Width of sub-roll | 500mm |
| Diameter of sub-roll(max)mm | φ300mm |
| Core specification of sub-roll | 3",2", 1" |
| Overall dimensions (L×W×H) | 1.4×1.1×1.1m |
| Weight | 0.7T |

Ⅳ. Quotation (F.O.B Price to Ningbo port)

| Model | Price |
| --- | --- |
| DYRW-500 | 4500USD |

Our price valid period last for 1 months.

Ⅴ. Delivery

Within 20 days shipment the machine，we manufacture the machine after we receipt 30%deposit.

Payment: 100% T/T

Guarantee period: 1 year

Packing: with stretch film and bubble film.

It also can be packing with wooden box (you need to pay the extra fee)