| WFQ-1700 Computer Control Vertical Film Slitting Machine Directory listing A. Feature-------------------------------------------------------------------------------- B. Main technical parameter ---------------------------------------------------------- C. Sample of product---------------------------------------------------------------------- D. Quotation----------------------------------------------------------------------------- E. Others---------------------------------------------------------------------------------- Price: F.O.B NINGBO 8500.00 USD,Price validity 20 days. Staff: only one worker examines a particular time. Outline dimension:2800×1200×1450 mm |
| --- |
| A.Feature: 1. The machine is a kind of vertical separating and cutting machine, rolling and releasing can be in front of or at the back of the machine. 2. Independent master control screen, more flexible and even easier operation. 3. Automatic deviation-rectifying of releasing, photoelectric eye is suitable for tracking the edge and color of transparent material. 4. Releasing tension adopts magnetic powder clutch control. 5. Rolling adopts magnetic clutch control. 6. Automatic slitter edge blowing-inhaling device. 7. Automatic meter counting of material moving length. This machine is suitable for separating and cutting such various roll materials as BOPP, PET, CPP, CPE, PVC, Aluminum foil and paper, etc. And can cut edge, separate and cut material according to different requirements during production. |
| B.Main Technical Parameter |
| Model | WFQ-1700 | WFQ-1300 |
| Max. material width | 1700mm | 1300mm |
| Min. Slitting Width | 100-1700mm | 10-1300mm |
| Max. mechanical speed | 50-200m/min | 50-180m/min |
| Accurate of adjustment | ±0.5mm | ±0.5mm |
| Tension control range | 0-50N.m | 0-50N.m |
| Max. original roll diameter | 800mm | 800mm |
| Paper inner Diameter | 76mm | 76mm |
| Max. Diameter of rolls after slitting | 450mm | 450mm |
| Total power | 6KW | 4.8KW |
| Voltage | 220V | 220V |
| Weight of machine | 2600KG | 1800KG |
| Overall dimension(L×W×H) | 2800×1200×1450mm | 2450×1300×1500mm |
| CUTTING TYPES: RAZOR TYPE BLADE AND DISC TYPE BLADES |
| MATERIALS: 50 GSM CRAFT PAPER, BOPP 30 GSM, PE 10 TO 20 MICRONS, METALIZED LAMINATED WITH PE 40 GSM |
| C. Sample of the product |
| D.Quotation (F.O.B Price to Ningbo port) |
| Model: | WFQ-1700 |
| Price: | 8500 USD |
| Delivery: | Within 25 days shipment the machine, we manufacture the machine after we receipt 30% deposit, other 70% balance should be paid before we delivery the machine. |
| Payment: | 100% T/T or 100% L/C |
| Guarantee | One year guarantee the quality of machine. But the buyer need pay the cost of maintenance if it is break down due to incorrect operation. Spare parts attached for free, problem parts can be changed for free in 1 year, but the express fee should be paid by users, others(if needed) suggest to be bought at the first time to save the cost of transportation. |
| Technical services: | We will teach your staff to learn all the operation instruction in our factory if needed, this operation is easy to learn and only 1 person is enough to control ! If need our engineer go to your country or teach and install ,the flight fee, the living fee, engineer salary (60 USD/per day) should be in charge by buyer We would present buyer the specification and Video or CD along with the machine when shipment. |
| Package： | In wooden box ,stretch film package or in bulk just according to the situation of shipment or clients. |
| valid period: | Our price last for 2 months. |
| E. Other * This type machine absorbs the domestic and foreign advanced technologies，which is a high tech product, researched and developed by ourselves. Our factory reserve the right of change the certain structures (to cause it more advanced) and the parameters, in order to provides better equipments Payment Thirty percent (30%) of total contact price amounting shall be paid by telegraphic transfer to bank which is appointed by the seller as down payment within fifteen (15) days after the date of the signed contract. In case the buyers cancel the contract by their own reasons, the sellers shall not refund the down payment to the buyers. Seventy percent (70%) of the total contract amount shall be paid by T/T before delivery after inspection and acceptance by the buyer in seller's workshop. REMARK All bank chargers in China are on seller's account All bank chargers outside China are on buyer's account. |