200A Oil Press machine

This machine is suitable for the extraction of vegetable oils from such oil-bearing materials as rape seed, peanuts, sesame seed, cotton seed, Soya beans, coconuts, tea seed, sunflower seed, etc. (The pressing worms can be replaced as required by the user for the purpose of the extraction of oils from some other oil-bearing materials, such as rice bran oil and the like.).

Technical data:

1、Capacity (The treating capacity for seeds)

| Name of oil seed | Capacity （kg/24h） | （%）Oil yield | （%）Residual oil in dry cake |
| --- | --- | --- | --- |
| Rape seed | 9000～10000 | 33～38 | 6～7 |
| Peanuts | 9000～10000 | 38～45 | 5～6 |
| Sesame seed | 6500～7500 | 42～47 | 7～7.5 |
| Cotton seed | 9000～10000 | 30～33 | 5～6 |
| Soya beans | 8000～9000 | 11～14 | 5～6 |
| Sunflower seed | 7000～8000 | 22～25 | 8～9.5 |
| Rice bran | 10000-12000 | 10～14 | 7～8 |

2、Inside diameter of steaming kettle：     φ1220 mm；

3、Stirring shaft speed：                 35 rpm；

4、Steam pressure：                     5～6 kg/cm2；

5、Pressing bores：   Front section   φ180 mm；   Rear section   φ152 mm；

6、Pressing worm speed：                    8 rpm；

7、Feed shaft speed：                     69 rpm；

8、Pressing time in cape：              2.5 min；

9、Seed steaming and roasting time：    90 min；

10、Max. temperature for seed steaming and roasting：125-128 ℃；

11、Power demand：                          18.5 kw；

12、Overall dimensions (L×W×H)： 2850×1850×3270mm；

13、Weight：                                     5000 kg

*  All such main parts of this machine as worm shaft, pressing worms, cage bars, gears and so forth are made of high-grade alloy steel through hardening treatment. As a result, in spite of the conditions of high temperature and abrasion under which they work day and night, they keep durable for a considerable period.

*  The combination of steaming and roasting is also one of the features of this machine. It can be regulated in accordance with the varied requirements of various oil-bearing materials for the temperatures before pressing so as to get high quality oils.

*  The whole process from feeding, steaming, roasting up to the discharge of oil and cake goes, on automatically and continuously, so it is easy to operate the machine, which results in the saving of labour.

Heating Mode: Steam

- Inside Diameter of Steam Boiler: ø 1220mm,
2. Steam Pressure: 5~6 kg/cm2,
3. Max.Temperature for Seeds Steaming and Roasting: 110~128℃,

Machine de presage de l’huile  Prix: USD 10,950.00 /Unité,

FOB Shanghai，Chine, avec moteur, emballé

Délai de livraison: 7~10 jours après la reception de prépaiement

Validité: un mois

- Limite de paiement

1) Si le montant est inférieur à 10,000 de dollars, le prépaiement est 100% par T / T.

2) Si le montant est supérieur à 10,000 de dollars, 30% comme le prépaiement par T / T, le solde de 70% doit payer avant la livraison.

- Conditions de garantie de la qualité

La durée de garantie de la qualité est un an. Toutes les pannes qui sont causées par la machine soi-même, la qualité sera responsable par le fabricant. Les autres pannes qui sont provoquées par le fonctionnement l'erreur de l'opération, les problèmes artificielles etc, seront responsable par le client soi-même.

- Situation de l'électricité

Toutes les machines énumérées ci-dessus fonctionnent sous la situation d'électricité qui répond à la norme chinoise: 380 Volts, 50Hz, 3 phases. Si les clients ont des exigences particulières sur  l'électricité des machines, les clients doivent payer le coût supplémentaire pour le besoin spécial d'électricité.

Si vous avez des questions ou des conseils, s’il vous plait contactez-nous librement.

Nous vous remercions et cordialement!