Wood Pellet Packing Machine

- Technical Parameters:

| Precision | : +/-0.2% |
| --- | --- |
| Packing speed | : 150~180bags per hour |
| Weighing scale | : 5kg-50kg per bag |
| Power Supply | : 4N-380Va.c |
| Power Dissipation | : ≤1.5KW |
| Compressed Air | : 0.3-0.5MPa |
| Compressed Air Consume | : 0.2m3 / min |
| Weight | About 300kg |
| Dimension | 3000*800*1700mm |

2．Advantage:

◆ High-precision sensors , high intelligent weighing controller , high accuracy , stable performance.

◆ blanking automatically correct poor , auto zero tracking , overshoot detection and suppression, and less excessive amount of alarm .

◆ Analog state enforcement capabilities , real fault diagnosis, easy maintenance and repair .

◆ Manual state enforcement capabilities , automatic control process fails once , as an emergency measure , all the packaging process can be done manually , without interrupting packaging operations .

◆ number of packages installed , installed automatic statistical package volume . With RS232 serial port, printer port, and computer communications , data printing.

◆ Adopt pneumatic actuator , cylinder inlet and outlet pressure adjustable , more reliable and non-polluting. And material contact parts made ​​of stainless steel , in line with food hygiene requirements , corrosion resistance, extended equipment life.

◆ Security engage in quality design, pneumatic components , electrical, instrumentation have security protection, ensure that the equipment , personal safety.

◆ Humanized design . Package quantity is changed, automatically adjust the conveyor height is very convenient , sewing machine automatic cutting line ; conveyor located reverse switch , for a suture defective packaging, returnable secondary suture.

FYI

◆ 采用高精度传感器、高智能化称重控制器，计量精度高、性能稳定。

◆ 落料差自动修正、零点自动跟踪、过冲检测与抑制，过量与欠量报警。

◆ 模拟状态下的强制执行功能，真正实现故障自诊断，方便维护与检修。

◆ 手动状态下的强制执行功能，一旦自动控制过程出现故障，作为应急措施，可手动完成全部包装过程，无须中断包装作业。

◆ 装包数、装包量自动统计。具有RS232串行口、打印机接口，可与计算机通讯，实现数据打印。

◆ 采用气动执行机构，气缸进、出口压力可调，工作更加可靠、无污染。与物料接触部件选用不锈钢，符合食品卫生要求，抗腐蚀，延长设备使用寿命。

◆ 安全性搞质量设计，气动元件、电器、仪表均有安全保护，确保设备、人身安全。

◆ 人性化设计。包装量改变时，输送机高度自动调节非常方便，缝包机自动剪线；输送机设后退开关，对于有缝合缺陷的包装，可退回二次缝合。

3．Main Structures:

3.1 filling system

3.2 weighting balance

3.3 belt conveyor

3.4 Semi-Auto Sewing Machine (By foot switch)

3.5 Electronic control cabinet

4．Flowing Process:

Manual bag placing-->Auto filling-->Auto weighting--> bag discharge--> bag conveyor-->Semi-Auto Bag Sewing Machine

ALIDITY OF THE QUOTATION:

This quotation is valid for 2 month only, since we get news that the price of steel will increase recently. So we can update the price 2 month later.

PAYMENTS:

100% T/T, the total sum is below USD5000 (including USD5000).50% prepayment by T/T, the balance 50% is paid after shipment when the total sum is above USD5000

WARRANTEE:

12 MONTHS from the date of commissioning, against any manufacturing defects. The guarantee does not include for the wear & tear parts, electrical and faults resulting in any accident/repairs unknown/unauthorized by us.

DELIVERY:

15-20 days from the date of receipt of the confirmed order along with prepayment.