HTS SMD LED DISPLAY FOR AV RENTAL USE

4mm pixel pitch, indoor die casting aluminum slim led displays

P4

The premium 4mm die casting LED display system for indoor use.

Fast & seamless assembly, superb image quality, wide viewing angles and unrivalled reliability.

Features:

- The cabinet thickness is only 75mm, the cabinet weight is only 9.5kgds/tile.

- Different color options of back cover according to clients requirements .

- 16 bit driver IC with rich and delicate colors , refresh rate at 3500Hz.

- Rotatable hanging lock and manual safety button avoid panels dropping off.

- Special design of back cover make sure different ways of maintenance .

- Adopt Die-casting aluminum housing, ensure the flatness of the screen and seamless among panels.

- Neutrik connectors are adopted, fast assembly, durable.

- Adopt the DC cooling fans, less noise for indoor use.

- Support hanging and stacking, suitable for both fixed install and rental activities.

P4  CABINET PHOTOS

CABINET FRONT VIEW

CABINET BACK VIEW

Technical specification

| Model | P4 |
| --- | --- |
| Pixel pitch | 4mm |
| Pixel configuration | 1R1G1B |
| LED type | SMD2020 |
| Module size | 256x256mm |
| Module resolution | 64x64 |
| Cabinet resolution | 128x128 |
| Cabinet size | 512x512mm |
| Density | 62500dots/㎡ |
| Brightness | ≥1200 NIT |
| Scan method | 1/16 |
| Best view distance | ≥4m |
| Max. power consumption | 300W/panel |
| Ave. power consumption | 180W/panel |
| Cabinet Weight | 9.5Kg |
| Grey scale | 16 bit、65536 step |
| Color | 281 billion |
| Refresh rate | ≥960 Hz |
| Best view | Vertical: 120°, Horizontal: 120° |
| Color temp | 7500K |
| Frame frequency | ≥60Hz |
| Out of control pixel rate | <1/10000 |
| MTBF | >5000 hours |
| Lifespan | 50000 hours |
| Signal input source | Composite, S-video, Component, VGA, DVI, HDMI, SDI, HD-SDI |
| Working voltage | AC 110/220v 50-60Hz |
| Control distance | Ethernet cable: 100m, Multi-mode optical fiber: 500m, Singel-mode optical fiber: 20km |
| Operation temperature | -20 to +40 |
| Working humidity | 10% to 80% |
| Protection level | indoor |

P4  SYSTEM CONNECTION DIAGRAM