PVC /WPC Windowsill & Door Board Production Line

◆Processing Flow Chart

Wood-Powder           PVC Powder               Caco3                 Other Agents

Mixing according to certain Formula proportion

Extruding

Various PVC windowsill                             Various PVC/WPC Door Boards

The waste can be 100% recycled after crushed and milled

◆Workshop Composition & Needed Equipment

| NO. | Name | Equipment | Power | Quan | Application |
| --- | --- | --- | --- | --- | --- |
| 1 | Mixing Workshop | Mixing units |  | 1 | Raw material mixture by formula, vibrating screen remove scum |
|  |  | plastic crusher |  | 1 | Break wastes into pieces |
|  |  | High-Speed Plastic Mill |  | 1 | Mill waste pieces into power for recycle |
| 2 | Extrusion Workshop | YF series PVC/WPC Wide Board Extrusion Line |  | 1 | Take mixed power into finial door board by extrusion device & moulds |
|  |  | Mould & die |  | 1 |  |
| 3 | Printing workshop | Laminating machine |  | 1 | Surface treatment |

◆Machine Specification

1. Mixing units

2. Plastic crusher

3. Plastic Mill

4. YF-series PVC/WPC Wide Board Extrusion Line

This line consists of Spring feeder, Main extruder, Vacuum shaping tank, YF-800 haul-off, Cutter, Stacker.

- TS Series Plastic Spring Feeder

2) Main extruder

3) Vacuum shaping box

4) YF-800 haul-off

- Cutter

- Automatic stacker

- PVC/WPC door board & PVC Windowsill Mould & Die

6.PVC windowsill & door board laminating machine

WUXI SENJIE PLASTIC MACHINERY CO., LTD

Address: NO.61 Renmin East Road, Yangshi Luoshe Town, Wuxi City, Jiangsu, China.

Tel: 0086-510-8021 9119   Mobile: 0086 13915229945   Fax: 0086-510-8021 9159

Attn: Sherry Wang   E-mail: wxsenjie@gmail.com  Website: www.sjsjcn.cn