Four-color Flexible Printing Machine

YT4600/4800/41000

1.Characteristics:

This machine is suitable for printing packing materials as polyethylene, polypropylene plastic bag, cellophane and roll paper, etc. And it is a kind of ideal printing equipment for producing paper packing bag for food, supermarket carry bag ,vest bag and clothes bag, etc.

- Easy operation, flexible starting, accurate color register.

- The meter counter can set printing quantity according to the requirements. Stop the

machine automatically at the set quantity or when the material is cut off.

- Lift and lower the printing plate cylinder manually, it will automatically stir the printing

ink after lifting.

- The printing ink is spread by the knurled cylinder with even ink color.

- Reliable drying system coordinated with high-speed rotation, it will automatically break

circuit when the machine stops.

6.360 continuous and adjustable register device.

7.The imported frequency control of motor speed adapts to different printing speeds, 8.There are Inching/Stopping buttons on the plate roller base and material rolling rack so                       as to make it easy operate the machine when the plate is installed.

2.Main Technical Variables:

| Model of Machine | YT4600 | YT4800 | YT41000 |
| --- | --- | --- | --- |
| Max.Width of Printing Material | 600mm | 800mm | 1000mm |
| Max.Printing Width | 560mm | 760mm | 960mm |
| Length Range of Printed Product | 191-914mm | 191-914mm | 191-914mm |
| Max. Diameter of Roll Material | 450mm | 450mm | 450mm |
| Printing Speed | 5-50m/min | 5-50m/min | 5-50m/min |
| Thickness of plate (Including Two-sided Glue paper) | 2.38mm | 2.38mm | 2.38mm |
| Total power | 10.87kw | 12.5kw | 14.37kw |
| Weight of Machine | 3000kg | 3500kg | 4000kg |
| Overall Dimension(L*W*H) | 4200*1600*2400mm | 4200*1800*2400mm | 4200*2000*2400mm |

- Picture:

4.Contact informations:

Ms.Vicky 
Xinye ( E-light ) Packaging Machine Co.,Ltd.
Website: http://xy.raxinye.com 
Skype; Xinye03
Tel:  86-577-65132727
Fax: 86-577-65132727
Mobile: 0086-13967703011
Add: No.104 Main Roadside, Yongguang, 
        Shangwang, Ruian, Zhejiang, China
P.C :325206

If you have any inquiry ,WARMLY welcome to call 86-13967703011 or email me,we’ll give you reply ASAP.