Fully Automatic Nonwoven Loop handle bag making machine

XY-600

1.Characteristics:

This machine applies for non-woven materials. It can make many kinds of bags

such as vest bags, Nonwoven Loop Handle Bag,loop handle bags, flat bags, box

bag, and ribbon-through bags for shoes and purse etc. It is equipped with computer

touch screen, step motor to control the length and photo electricity to track,

accurately and steadily. There are control devices like auto-counting alarming, auto-

punching etc., which make the finished products well-sealed and nice-cutting with

high speed and efficiency. It is an ideal environmental protection bag making equipment.

- Main Technical Variables:

| Model | XY-600 |
| --- | --- |
| Max. Bag-making Width | 550mm |
| Power | 220V(380V) |
| Air Compressor | 0.6-0.8Mpa |
| Total Power | 13.5kw |
| Output | 10-110pcs/min |
| Loop Handle Bag | 20-60pcs/min |
| Overall Dimension(L*W*H) | 11000*2950*2250MM |
| Machine Weight | 3500KG |

- Picture: