Zhejiang Deguang Machinery Co.,Ltd

www.wenzhoudg.com

shdg@wenzhouhg.com

Contact person:Kelvin

Tel:0086-577-65161881

Cell:0086-13626509930

Quotation:

Price:8200 USD Fob Ningbo（Wooden packing）

Delivery time:15 days after the deposit arrives.

Payment: TT 30% as deposit, TT balance before shipment.

1. Main parameter:

1. Max. width of slitting material: 1300mm

2. Min. width of slitting material: 40mm

3. Max. slitting speed: 200m/min.

4. Max. unwind diameter: 600mm

5. Max rewind diameter: 500mm.

6. Paper core diameter:76mm or 152mm

7. Machine power: Max 5kw

8. Air supply: 0.8MPa dry compressed air (1 compressor)

8. Overall dimension: 1550*2600*1500mm

9. Net weight: 1.1T

2. Unwind unit

1. Unwinding adopts magnetic brake (50N.M)

2. Unwinding adopts air shaft

3. Automatic tension control

4.Web guide precision: ±0.5mm

5. Web guide mode: Edge guide or line guide

3. Traction part

1. Pneumatic pressing roller(Φ110mm PU Material)

2. Traction roller(Φ112mm) is driven by frequency motor(4kw), transmitted by triangle belt.

3. Meter-counter can count the length of film accurately.

4. Slitting part

- Equipped with flat blade

- Equipped with ruler on the cutter pole which is convenient for cutter matching

5. Rewind part

- Rewinding adopts magnetic brake (50N.M), air shaft.

- Pressing rollers, two for each rewinding shaft

- Waste edge trim device, AC motor, 0.75KW

6. Frame

1. Solid cast iron base and wall board

2. Each guiding roller(ф100) has antislipping tape.

3. Unwinding, rewinding and controlling system in the same side

Spare parts list

| Name and description | Quantity | Notice |
| --- | --- | --- |
| Air compressor | 1 set |  |
| Operational manual | 1 piece |  |
| Hex Socket Spanner | 1 set |  |
| 8 Straight Screwdriver | 1 piece |  |
| 17～19 open spanner | 1 piece |  |
| 17～19 box spanner | 1 piece |  |