PF series Multi-Functional Crusher

- Uses and performance

This machine adopts impact crushing principle, the impact of the material into the crushing chamber, hammer rotary movement and materials with each other to achieve the purpose of crushing impact. Broken material the cyclotron gas driven through the sieve of the lower part of the body from the plane. Product particles size through a screen aperture control and regulation, is not up to the requirements of coarse particles in the crushing cavity multiple cycles broken from the plane through the screen and eventually all.

The machine has a small loss, high efficiency and satisfactory performance, reliable product quality, operational safety, and environmental health. It can be widely used in medicine, food, chemical, agricultural, sideline, construction and other industries, crushed into a powder ideal effect of broken brick rubble, cinder, sand, blocks and other materials. The hard shell of the animal and plant raw material is crushed into a smooth, delicate, and excellent performance fodder.

- Construct Overview

The machine is combining with an electric motor,-hammer(knife, ax)rotating body, feed port, base crushing chamber discharge port. Circular motion is combining with a motor driven spindle disk pendulum body of materials crushing operations.

- Technical Parameters

| models parameters | PF50 | PF85 |
| --- | --- | --- |
| Motor power ( KW ) | 4 | 7.5 |
| Spindle speed (r/min) | 1300 | 930 |
| Capacity (kg/h) | ~500 | ~1500 |
| Product fineness (mesh) | ≥60mesh | ≥60mesh |
| Weight (kg) | 180 | 310 |
| Hopper size B×Hmm | 340×130 | 380×170 |
| Dimensions L×B×Hmm | 1200×600×1100 | 1300×660×1250 |
| PRICE(USD) | 5,900 | 8,400 |

Shipping: FOB Port of Shanghai

Kevin

Xi Cun Powder Technology(Shanghai) Co.,Ltd

Room 510, Lizhou Business Center,383 East Huan Cheng Road,

Fengxian District, Shanghai

Tel:21-57413456

Fax:21-67105288

Mobile:18717960225

e-mail:trade@xicun-powder.com

web: http://powder-machinery.ru/