ALUMINUM FLEXIBLE DUCT FORMING MACHINE

This machine is specially for producing aluminum flexible ducts with pure aluminum foil or stainless steel without steel wire reinforcement for various purpose. Our advantage is our omnipotent mould which will save investment cost.

I Main technical data

1.1 Diameter range: 60mm~300mm

1.2 Length of aluminum tube: 100-8000mm

1.3 Suitable material: 42-55mm wide

Pure aluminum foil: 0.05-0.15 (code 8011, hardness H22)

stainless steel, 0.08-0.18mm

1.4 Working speed: 1-5m/min

1.5 Weight: about 250kg

1.6 Main motor power: 0.75kW

1.7 PLC control system, from Japan

1.8 Dimension: 1200mm x 550mm x 1200mm (main machine, excluding unloading rack)

1.9 Duct concentrating device: 3000mm x 480mm x 1500mm

II Buildup of the line:

2.1 Simple decoiler

2.2 PLC from Japan

2.3 Material of roller: GCr15 steel, quenched HRC58-62.

2.4 Manual cutting type

2.5 Unloading rack: 2 meters (if need longer tube, the rack should be more)

III Accessories:

3.1 Omnipotent mould, diameter range from 60 to 250mm, free adjusting.

3.2 Special steel strip as mould, 20 meters

3.3 Special tool, one set

3.4 Lubricant oil, one bottle

3.5 Duct contracting device

IV Price

Price basis: FOB Shanghai

Payment: 30% down payment by T/T, the balance by fax copy of B/L

Lead-time: within 40 days after receiving down payment

Unit price: EUR 7,550

V Guarantee: One year since the date of B/L