ZG-420 Thermoforming Vacuum Packaging Machine

(Main Configuration)

| Main Technical Parameters |
| --- |
| Model | ZG-420 |
| Width of top film (mm) | 400 |
| Width of bottom film (mm) | 422 |
| Max. roll diameter(mm) | Top roll 400mm /bottom roll 350mm |
| Forming depth (mm) | 30 |
| Core diameter (mm) | 75 |
| Package style | Vacuum & Gas Flush |
| Film | Flexible/ Semi-rigid/ Rigid |
| Electric power | Depend on country(Need to be confirmed) |
| Film feed | Automatically and available for blank and colorful film |
| Machine weight(kg) | 1900kgs Approximately |
| Machine overall dimensions | 5000X 900X1700mm |
| Main Electrical Parts: |
| Touch Screen Controller | Omron |
| PLC | Omron |
| Servo Motor & Driver | Panasonic |
| Contactor | Schneider |
| Solenoid Valve | MAC |
| Air Cylinder | SMC |
| Air Filter | SMC |
| Photocell for Pre-printed Film | SICK |
| Vacuum Pump | BUSCH (200m³ /hr; built in) |
| Vacuum Pump Model | BUSCH R5-0202D |
| Its main electrical parts are imported from Japan & Europe |
| Main Machine Structure: |
| Main Machine Body | Stainless steel |
| Mould Material | Teflon coated aluminum |
|  | Water cooling |
| Mould Size | According to Customer’s request |
| Chain | REGINA |
| Top Film Roller | Air-shaft(Mechanical brake) |
| Bottom Film Roller |  |
| Code Printer | Auto type printer |
| Cutting System | Horizontal punching cutting |
| Slitting Device | Vertical wheel cutting |
| Discharge Conveyor | 1000mm length |
| Scrap Recycling System | Rolling rewinding type |
| Machine Price: | FOB NINGBO USD55000 |
| Optional Equipments: |
| 1) Air-shafts with Magnetic powder tension brake system |
| 2) Automatic filling device requested by products |
| 3) Weight Measure 4) Labeling 5) Metal Detective |
| 6) BUSCH Vacuum Pump(100-1000m³ /hr. Different model; different cost) |
| Others: |
| Payment：30% T/T by advance, 70% T/T before shipment; after testing & inspected by client |
| Delivery Time: 90days after receiving the 30% deposit by T/T |
| Package: Export Plywood Case |
| Guarantee: 1 year since shipment date |
| Installation: Training the buyer’s worker in seller’s factory, or install the machine in buyer’s working place, buyer should charge of the cost(Including visa, round air tickets, food, hotel and daily salary) |
| Valid: 50days |

Contact: Gary

Date: 2012-08-02