Computer Control Film Sealing & Cutting Machine

Characteristics :

1.This machine can make both flat bags &vest bags. What’s more ,it can make 2 lines of bags with only 1 photo-eye.(We can also make machine with 2 photo-eyes, but the price is different)

2.It is equipped with computer to set the bag length & width, pieces and batches of bags you want to make, speed and temperature etc. with a photo-eye to track the printed film to make printed bags. It has such functions like auto-alarming, auto-stop, and auto counting etc.

Main Technical Variables:

| Model | GFQ-600 | GFQ-700 |
| --- | --- | --- |
| Max Width | 480-500mm | 650mm |
| Max Length | 1600mm | 1600mm |
| Sealing and Cutting Thickness | 0.006-0.10mm | 0.006-0.10mm |
| Bag -making Speed | 40-120pcs/min*2 | 40-120pcs/min*2 |
| Error in Length | ±1mm | ±1mm |
| Power of Main Motor | 1.1kw | 1.5kw |
| Heating Power | 1.2kw | 1.5kw |
| Total Power | 2.5kw | 3.2kw |
| Weight of Machine | 700kg | 820kg |
| Overall Dimension | 2650mm*1200mm*1550mm | 2650mm*1400mm*1550mm |

| Model | GFQ-900 | GFQ-1000 |
| --- | --- | --- |
| Max Width | 750mm | 1000mm |
| Max Length | 1600mm | 1600mm |
| Sealing and Cutting Thickness | 0.01-0.10mm | 0.01-0.10mm |
| Bag -making Speed | 40-120pcs/min*2 | 40-120pcs/min*2 |
| Error in Length | ±1mm | ±1mm |
| Power of Main Motor | 1.5kw | 2.2kw |
| Heating Power | 2kw | 2.5kw |
| Total Power | 4.3kw | 2.5kw |
| Weight of Machine | 850kg | 1100kg |
| Overall Dimension | 2800mm*1500mm*1550mm | 2900mm*1800mm*1750mm |

1).Trader terms: FOB Ningbo.

2).Payment: 30% of the total value of the contract should be paid by T/T to the Seller as deposit, the balance 70% of the total value should be paid by T/T  before shipment when goods ready.

3).Minimum order: 1 set

4).Delivery time: Within 30 days after receipt of advance.

5).Packaging: in wooden box.

6).Guarantee: one year

7).Validity of price: 3 months!

8).The seller agree to send one engineer to Buyer's factory for installation as requested by the Buyer, but all expenses shall be borne by the Buyer such as air ticket, hotel and food charge, (in one week),after 7 days, the Buyer should pay the engineer 80 USD/day as subsidy.

Production Line:

The Samples:

Workshop:

Packaging&Shipping:

Certificates:

Exhibition:

Our Offices:

I'm always here waiting for you!