ABOUT US

Established in June 2007, Wenzhou Tianye Plastic Machinery Co., Ltd. (with its headquarters in Hefei) is a manufacturer specialized in producing whole-set equipment for PP, PE woven bags, mesh bags and flexible freight bags. With total assets of RMB 50 million Yuan, our company is a member unit of China Chamber of Commerce for Import and Export of Machinery and Electronic Products, China Packaging Association and Plastic Machinery Industry Association. We have been certified to the ISO9001 international quality system and have obtained the right of independently managing import and export. In addition, we have been granted many national and international patents for five consecutive years.

Our company provides customers with whole-set equipment for plastic woven bags, cement woven bags, mesh bags, film blowing bags and mulch film bags, flexible freight bags, woven bags, supermarket shopping bags, etc. Our products are sold well in more than 20 provinces and cities throughout China and exported far to Mid East, Africa and other countries and areas, winning good reputation in the world with their excellent performance, good quality and considerate service.

Thanks to the support from Hefei Tianfeng and our five years of efforts, Wenzhou Tianye Plastic Machinery Co., Ltd. has become a star enterprise in the plastic machinery industry. We have established companies in Hefei of Anhui and Shandong, set up woven bag plants and joint ventures in Indonesia and Nigeria, and developed many agents at home and abroad, which have laid a firm foundation for the development of our enterprise.

We wish new and old customers to discuss business with us through phones and emails. We hope that our products and experience will create more profits and better development opportunities for you.

Machinery List

| No. | Description | Specification |
| --- | --- | --- |
|  | Normal PP Yarn Extrusion Line | SJ-FS5.5 |
|  | 4-shuttle or 6-shuttle Circular loom | SBY-750×4S SBY-850x6S |
|  | YT Series Flexible Letter Press | YT-4600, YT-4100 |
|  | Automatic cutting machine for woven bags | HF-800A |
|  | Automatic sewing machine for woven bags | HF-1500 |
|  | Recycling Machine | SJ-FJ-100 |
|  | Dry machine | SH-30 |
|  | Crusher machine | SCP-300 |
|  | Baling Machine | DB-100 |

SPECIFICATION OF MAIN MACHINE

1. SJ-FS5.5 Plastic Tape Extruding & Stretching Machine

This machine uses the PP or HDPE material to produce tapes for PP woven bags weaving through production procedures of material heating& extruding, splitting the film into tapes, tapes stretching & forming and tapes winding on the bobbins by winding machine; then put the bobbins with tapes on circular loom for weaving. This machine can use all kinds of materials, such as 100% recycled materials, power materials or pellet materials. Its screw and cylinder and other important parts adopt special alloy steel.（This whole set has included winding machine and drying mixer）

| Main scheme name | Type & Parameter | Quantity |
| --- | --- | --- |
| System power | 98Kw |  |
| A．Extruding machine |  | 1 |
| Cooling style of Gear Case |  |  |
| Diameter of screw | φ110mm |  |
| L/D of screw | 20:1 |  |
| Speed of screw | 10-55r/min |  |
| Material of screw | 38CrMoAlA |  |
| Material of screw bobbin | 38CrMoAlA |  |
| Hydraulic inductor |  |  |
| Heated scope | 6 |  |
| Heated power | 24Kw |  |
| Heating style | Heating loop of casting Al |  |
| Power of main engine | 30Kw |  |
| Volume of extruding | 80Kg/h |  |
| B.Device of changing net |  | 1 |
| Style of changing net | Common Changing net |  |
| Scope of heating |  |  |
| Power of heating |  |  |
| Heating style |  |  |
| C．Mold |  |  |
| Width of mold | 600mm | 1 |
| Extent of heating |  |  |
| Scope of heating | Heating board of casting Al |  |
| Power of heating |  |  |
| Adjusting scope of mold width | 0.1-1 |  |
| D．Device of Water Cooling |  |  |
| Cooling Water Case |  | 1 |
| Dimension of Water Case |  |  |
| E．Separating into pieces Device |  |  |
| Style | Machine |  |
| Width of each piece | 4-13 |  |
| F．Stretching Machine |  |  |
| Diameter of Stretching roller | 320mm | 1 |
| Main scheme name | Type & Parameter |  |
| Power of Tow engine | 5.5Kw |  |
| Drive style | Chain Drive |  |
| Speed of Stretching | 20-150m/min |  |
| G．Heating Plate for Tape of Stretching |  | 1 |
| Style | Arc Plate |  |
| Size | 3700×600mm |  |
| Heating power | 15 |  |
| H．Heating Plate for Tape Forming |  | 1 |
| Style | Arc Plate |  |
| Size | 2200×600mm |  |
| Heating power | 12Kw |  |
| I．Driving Unit for Tape Forming |  | 1 |
| Dia. of Roller | 320mm |  |
| Drive Style | Chain Drive |  |
| J.Winding Unit |  | 1 |
| Style | Electric magnet or Mechanical Drive |  |
| Dia of Bobbin | φ38mm |  |
| Length of Bobbin | 230mm |  |
| Winding Spindles | 100 |  |
| Dia. Of Tape Winding |  |  |
| Width of Tape | 1.8-3 |  |
| Motor Power for one Spindle |  |  |
| K．Overall Dimension | 23500×2500×1800mm |  |
| Weight | 8000Kg |  |

2. Circular Loom

This series circular loom is used for weaving flat PP/HDPE yarn to tube cloth, it had developed from our long time research and manufacture experience with adopting advanced technology from domestic and abroad. It can weave different quality flat yarn even complete recycled material. Reasonable design, proper structure, easy operation, convenient maintenance, low power consumption and high efficiency etc.

★ New surface cam driving structure;

★ Rimless wheel shuttle style, less friction, more steady running;

★ Latest weft &warp detecting system, lower waste, higher efficiency;

★ New weft automatic feeding system, reducing waster;

★ Automatic synchronization controller to guarantee smooth cloth;

★ Maxim rotary speed 180rpm with 2.7m/min output (10*10), faster, steadier, lower consumption.

The main technical parameters:

| Model | SBY-750/4S | SBY-850/6S |
| --- | --- | --- |
| Number of shuttle | 4pcs | 6pcs |
| Maximum speed of the host | 180rpm | 150rpm |
| Fabric folded path | 300-750mm | 300-850mm |
| Power of main motor | 2kw | 3kw |
| Maximum diameter of weft yarn | 95mm | 95mm |
| The maximum diameter of organzine | 135mm | 135mm |
| Root of the number of warp (pc) | 640pc | 720pc |
| The total weight | 1.9t | 1.9t |
| Dimensions(L*W*H) | 9.0 *2.2 *3.2m | 9.6 *2.8 *2.9m |

## 3. YT Series Flexible Letter Press

Product Details:

This machine is suitable for printing packaging materials like PP, PE plastic bags, glass paper and roll paper, etc. And it is a kind of deal printing equipment for packing bag for food, supermarket handbag and clothes bag, etc.

Characteristics:

1. Easy operation, flexible starting and accurate color register

2. The meter counter can set printing quantity according to requirements. Stop the machine automatically at the set quantity or when the material is cut off

3. Manually printing plate cylinder, automatic mixing ink after lifting

4. The printing ink is spread by the knurled cylinder with even ink color

5. Reliable drying system coordinated with high-speed operation, automatic shutdown circuit.

6. The 360-degree continuous and adjustable longitudinal flowers device

7. The imported of frequency control motor, which adapts to different printing speeds

8. There are inching/stopping buttons on the plate roller base and material rolling rack so as to make it easy to operate the machine when the plate is installed

The main technical parameters:

| model | YT-4600 | YT-4100 |
| --- | --- | --- |
| Maximum width of printed material | 600mm | 1000mm |
| Maximum printing width | 560mm | 960mm |
| Length range of printed materials | 191-914mm | 191-914mm |
| Coil diameter | φ450mm | φ450mm |
| Printing speed | 5-50m/min | 5-50m/min |
| Plate thickness (including double-sided adhesive tape) | 2.38mm | 2.38mm |
| Total power | 10.87kw | 14.37kw |
| Weight (approx.) | 3000kg | 4000kg |
| Dimensions (L * W * H) | 4200*1600*2400mm | 4200*2000*2400mm |

Note: The product of our company may always be updated, and are subject to change without notice (the real products shall prevail).

4. Woven Bag Auto-cutting Machine

##### Detailed Product Description

It is applied to cutting reeled woven bags or poly bags at fixed cutting step or cutting via tracking the mark.

As combination of mechanism, electronics and optical system, it features chip system and high precision step motor for cutting control, numeral-control for cutting length, and mark tracking capacity for cutting. Users can select manual or auto function for working.

Moreover, users can preset the instruction to fold the cut bag in a certain quantity, as the machine can count the cut bag automatically with a sound and optical warning system. Its unwinding system is equipped with an electric hoist for material loading, optical-electric speed convertible motor for material feeding; and its final stacking system is the auto optical-electrical rack. It’s wide in application, stable in performance, and easy in operation

The main technical parameters:

| Model | HF-800 |
| --- | --- |
| Power of motor | 2.2kw |
| Max cutting width | 800mm |
| Max cutting length | 1250mm |
| Max Capacity | 70pc/min |
| Unwinding power | 0.75KW |
| Overall dimension | 4500*1650*1000mm |
| Weight | 950kg |

##### 5. Woven Bag Auto-sewing Machine

Characteristics:

This machine can work with woven bag cutting machine. It equipped with a break line automatic stop alarm device. It avoids secondary, and the seam can be single or double ruffled.

The main technical parameters:

| Model | HF-1500 |
| --- | --- |
| Power of motor | 1kw |
| Max sewing width | 900mm |
| Max sewing length | 1500mm |
| Max Capacity | 20-40pcs/min |
| Air Compressor Pressure | 0.4Mpa |
| Stitch Length | 5-16 mm |
| Overall dimension | 1700×1900×1100mm |
| Weight | 600kg |

## 6. Drying Mixer

## Product detail:

## This machine is mainly used for mixing and drying polypropylene, polyethylene, fill materials and other additives. Then these materials will be prepared for wire drawing machine, coated composite machine, film blowing machine to produce flat, coated composite, blown film.

The main technical parameters:

| Model | SH-30 |
| --- | --- |
| Power | 15kw |
| Production capacity | 150-300kg/h |
| Weight | 500kg |
| Dimensions | 1500×600×1400mm |

## 7. Recycling Granulator

## Product Details:

## This machine can process the old recycling bags, film or other plastics into raw materials for plastic. The screw and barrel of the machine use 38CrMoA1A alloy steel, and the die heats with automatic temperature control.

## The main technical parameters:

| Model | SJ-FJ-100 |
| --- | --- |
| Screw diameter | 100mm |
| Screw | Main screw 13:1 vice screw 11:1 |
| Screw speed | 50-60r/min |
| Main motor power | 11kw |
| Electrical machine power to pay | 5.5kw |
| Pelletizing Power | 0.37kw |
| Heating power | 12kw |
| Production capacity | 30-80kg/h |
| Weight | 900kg |
| Installation Dimensions (L * W * H) | 4500 *2000 *1100mm |

## 8. Plastic Crusher

Product Details:

This machine is mainly used to smash waste silk, rejected products and scrap during the production of plastic woven bags for the using of producing flat yarn or for recycling.

The main technical parameters:

| Model | SCP-300 |
| --- | --- |
| Power | 7.5kw |
| Blade width | 300mm |
| Number of blades | 6 |
| Production capacity | 30-50kg/h |
| Weight | 400kg |
| Dimensions | 1050 *800 *1370mm |

Note: The product of our company may always be updated, and are subject to change without notice (the real products shall prevail).