QT10-15 Production Line Price

| No | Name | Specification | Unit price× Qty. | Images |
| --- | --- | --- | --- | --- |
| I Batching System |
| 1 | 45 ton cement silo (for reference not including the total price ) | Capacity | 45tons | Supplied by customer |  |
|  |  | Diameter of tank | 2.2 m |  |  |
|  |  | Thickness of tank | 5mm |  |  |
|  |  | Total height | 11 m |  |  |
| 2 | Screw Conveyor (for reference not including the total price ) | Diameter (mm) | 219 mm | 2200×1 Set |  |
|  |  | Wall thickness(mm) | 8mm |  |  |
|  |  | Handling Capacity (m3/h) | 34tm3/h |  |  |
|  |  | Power (kw) | 5.5 kw |  |  |
| 3 | Cement Scale (for reference not including the total price ) | Volume of Weighing Hopper | 0.4m3 | 1300×1 Set |  |
|  |  | Batching Precision | ±1％ |  |  |
|  |  | Max. Metage of Powder Material | 500kg |  |  |
|  |  | Max. Metage of Water Scale | 180kg |  |  |
| 4 | PL1200 Concrete Batching Machine | Cubage of weighing hopper | 1.2 m³ | 7900×1 Set |  |
|  |  | Cubage of reserve hopper | 3×3m³ |  |  |
|  |  | Productivity | 60m³/h |  |  |
|  |  | Max. metage | 2000 kg |  |  |
|  |  | Batching category | 3 |  |  |
|  |  | Dimension（L×W×H)mm | 8390×2000×2800 |  |  |
| 5 | JS750 concrete mixer | Input Capacity | 1200L | 8900×1 set |  |
|  |  | output Capacity | 750L |  |  |
|  |  | Productivity | ≥25m3/h |  |  |
|  |  | Max. raw diameter material | 80/60 mm |  |  |
|  |  | Roating speed of stirring shaft | 2*7r/min |  |  |
|  |  | Dimension ((L×W×H)mm | 4195×2300×2800mm |  |  |
|  |  | power | 38.6KW |  |  |
|  |  | Weight | 6800kg |  |  |
| 6 | Belt Conveyor | Length | 6 m | 1500x1 set |  |
|  |  | Width | 50 cm |  |  |
|  |  | power | 2.5kw |  |  |
| Ⅱ、Forming Section |
| 6 | Block making machine | Block Making Machine | 1pices | 53900×1 Set |  |
|  |  | Hydraulic Unit | 1 piece |  |  |
|  |  | PLC Control Unit | 1 piece |  |  |
|  |  | Pallets Feeder | 1 piece |  |  |
|  |  | Block sweeper | 1 piece |  |  |
|  |  | Spare parts and tools | 1 piece |  |  |
|  |  | mould | 1set |  |  |
| 7 | color feeding system | Color Feeding System | 1 Set | 8000×1 Set | Optional ( for paver with color making) |
|  |  | JQ350 Mixer | 1 Set |  |  |
| Ⅲ.transferring Section |
| 8 | transferring equipment | Automatic Blocks Stacker | 1 sets | 6200×1set |  |
|  |  | Manual Hydraulic Cart | 2 pieces |  |  |
| Total FOB Qingdao Price | 84900USD |
| Container: Equipment No.4~8 requires 3×40 feet container (40HQ) |
| IV.Optional Accessories |
| 9 | Color feeding machine | Color Feeding System | 1 set | 8000x1 set | Optional ( for paver with color making) |
|  |  | Conveyor Belt | 1 set |  |  |
|  |  | JQ350 Mixer | 1 set |  |  |
| 10 | Pallet | PVC pallet/Bamboo pallet | 1300x900x25/30mm | 1200 pcs. |  |
| 11 | Extra mould | Block mould | 1 set | 3400USD | (Including hollow block,solid block) |
|  |  | Paver mould | 1 set | 3700UISD | (Including all kinds of paver,interlock,curbstone) |

# Block And Paver General Capacity List

| Size(LxWxH) | Pcs/Mould | Pcs/ Hr | Pcs/ 8 Hr |
| --- | --- | --- | --- |
| 400X100X200 | 20 | 3000-3600 | 24000-28800 |
| 400X150X200 | 14 | 2520-2940 | 20160-23520 |
| 400X200X200 | 10 | 1800-2100 | 14400-16800 |
| 400X250X200 | 8 | 1200 | 9600 |
| 230x110x70 | 42 | 7500-8800 | 60000-70400 |
| 200X100X60 | 35 | 6300 | 51400 |
| 200X163X60 | 20 | 3600 | 28800 |
| Can make all kind of hollow and solid and paver block，widely used in building, road pavings, squares, gardens, landscaping, city constructions, etc. |

QT10-15 Host Machine Parameter

| Dimension of host machine | 3500×2220×2850m | Host machine power | 45.38KW |
| --- | --- | --- | --- |
| Moulding area | 1025×810mm | Vibration force | 100KN |
| Moulding period | 15-25S | Mixer model | JS750 |
| Weight of the host machine | 14T | Factory area | 300㎡ |
| The size of the pallet | 1300×900×30mm | General water Consumption | 12T/every da |

# Main Raw Material

# Stress and Strength : 10-15MPA(to increase the strength, it will need to change the mix design)

| No | NAME | Proportional ration | Sample |
| --- | --- | --- | --- |
| 1 | cement | 10% |  |
| 2 | sand | 30% |  |
| 3 | Crushed stone | 60% |  |