Two Colour Flexible Printing Machine

Characteristics :

This machine is suitable for printing such packing material such as polyethylene,  polypropylene plastic  bag,  cellophane  and  roll paper etc.  And it  is a kind  of ideal printing equip-ment  for  producing  paper packing  bag for food,  supermarket  carry  bag,  vest bag  and clothes bag, etc.

Performance and features:

1. Easy operation, flexible starting, accurate colour register.

2. The meter counter can set printing quantity according to the requirements. Stop the machine automatically at the set quantity or when the material is cut off.

3. Lift and lower the printing plate cylinder manually. It will automatically stir the printing ink after lifting.

4. The printing ink is spread by the knurled cylinder with even ink colour.

5. Reliable drying system coordinated with high-speed rotation, it will automatically break circuit  when the machine stops.

6. 360°continuous and adjustable longitudinal register device.

7. The imported frequency control of motor speed adapts to different printing speeds.

8. There are Inching/Stopping buttons on the plate roller base and material rolling rack so as to make it easy operate the machine when the plate is installed.

Main Technical Variables

| Model of Machine | YT-2600 | YT-2800 |
| --- | --- | --- |
| Max.Width of Printing Material | 600mm | 800mm |
| Max.Printing Width | 560mm | 760mm |
| Length Range of Printed Product | 191-914mm | 194-914mm |
| Max.Diameter of Roll Material | 450mm | 450mm |
| Printing Speed | 5-50m/min | 5-50m/min |
| Tchickness of plate(Including Two-sided Glue Paper) | 2.38mm | 2.38mm |
| Total Power | 8kw | 10kw |
| Weight of Machine | 1800kg | 2000kg |
| Overall Dimension(L*W*H) | 2300*1860*2145mm | 2300*2060*2145mm |
| Model of Machine | YT-21000 |  |
| Max.Width of Printing Material | 1000mm |  |
| Max.Printing Width | 960mm |  |
| Length Range of Printed Product | 191-914mm |  |
| Max.Diameter of Roll Material | 450mm |  |
| Printing Speed | 5-50m/min |  |
| Tchickness of plate(Including Two-sided Glue Paper) | 2.38mm |  |
| Total Power | 12kw |  |
| Weight of Machine | 2200kg |  |
| Overall Dimension(L*W*H) | 2300*2260*2145mm |  |

Production Line:

Samples:

Certificates:

Our Packaging:

1).Trader terms: FOB Ningbo.

2).Payment: 30% of the total value of the contract should be paid by T/T to the Seller as deposit, the balance 70% of the total value should be paid by T/T  before shipment when goods ready.

3).Minimum order: 1 set

4).Delivery time: Within 30 days after receipt of advance.

5).Packaging: in wooden box.

6).Guarantee: one year

7).Validity of price: 3 months!

8).The seller agree to send one engineer to Buyer's factory for installation as requested by the Buyer, but all expenses shall be borne by the Buyer such as air ticket, hotel and food charge, (in one week),after 7 days, the Buyer should pay the engineer 80 USD/day as subsidy.