# QT40-3A production line Price

| No | Name | Specification | Unit price× Qty. | Images |
| --- | --- | --- | --- | --- |
| 1. Batching system |
| 1. | JD350 mixer | Input Capacity | 560L | 800×1 set |  |
|  |  | output Capacity | 350L |  |  |
|  |  | Productivity | ≥4m3/h |  |  |
|  |  | Max. raw diameter material | ------------ |  |  |
|  |  | Rotating speed of stirring shaft | 4r/min |  |  |
|  |  | Dimension ((L×W×H)mm | 1350×1350×1250mm |  |  |
|  |  | power | 10.5KW |  |  |
|  |  | Weight | 420kg |  |  |
| Ⅱ、Forming Section |
| 6 | Block making machine | Block Making Machine | 1pcs | 3600×1 set |  |
|  |  | Spare parts and tools | 1 set |  |  |
|  |  | mould | 1set |  |  |
| Total FOB Qingdao Price | 4400USD |
| Note:Total about 8 Cub, we usually use LCL |
| Ⅲ.Optional Accessories |
| 7 | Extra mould | Hollow block mould | 1 set | 700USD |

# Block general capacity list

| Size(LxWxH) | Pcs/Mould | Pcs/ Hr | Pcs/ 8 Hr |
| --- | --- | --- | --- |
| 400X100X200 | 7 | 840 | 6720 |
| 400X150X200 | 5 | 600 | 4800 |
| 400X200X200 | 4 | 480 | 3840 |
| 400X250X200 | 3 | 360 | 2880 |
| Just for reference, we wil give the exact capacity according your block dimension |

QT40-3A Host machine parameter

| Dimension of host machine | 1800×1400×1100mm | Host machine power | 5.2KW |
| --- | --- | --- | --- |
| Voltage | 220V/380V/415V etc | Vibration force | 35.5KN |
| Moulding period | 25S | Mixer model | JD350 |
| Weight of the host machine | 0.8T | The size of the pallet | No need |

# Main raw material

# Stress and Strength : 10-15MPA(to increase the strength, it will need to change the mix design)

| No | NAME | Proportional ration | Sample |
| --- | --- | --- | --- |
| 1 | cement | 10% |  |
| 2 | sand | 30% |  |
| 3 | Crushed stone | 60% |  |