# PROJECT

##### FOR

FL-300 FLUID BED GRANULATOR

&

GFG-300 Fluidizing Dryer

BY

Jiangsu Xianfeng Drying Engineering Co., Ltd

China

Fluid bed granulator

FL-300 Fluid bed granulator

Technical Parameters：

| Item | Unit | parameter |
| --- | --- | --- |
| Diameter of container | mm | 1600 |
| Container volume | L | 1000 |
| Capacity | Kg/batch | 150-350 |
| Power of fan | kW | 30 |
| Electrical heater | kW | 90 |
| Amount of compressed air | M3/min | 2.0 |
| Compressed air pressure | MPa | 0.6 |

Detailed parts：

| Name | Spec | Material and type | Manufacturer |
| --- | --- | --- | --- |
| Main machine system | filtering chamber(Top chamber)： dust remove and filter system with shaking cylinder, | SUS304 Flange δ=16 Main machine δ=3mm Granulating system include peristaltic pump, spray dryer | Xianfeng |
|  | Middle chamber SUS304 With spray nozzle(two fluid), peristaltic pump |  |  |
|  | One trolley: SUS304 |  |  |
|  | Top-lift section：2 air cylinder and ballonet air-sealing |  |  |
|  | Inlet air chamber ：with inlet air adjust air flap , inlet-air filter and heater, drainage |  |  |
|  | Support: stainless steel SUS304 |  |  |
|  | Seal ：silicon rubber |  |  |
|  | Temp point ：inlet one ，outlet one |  |  |
| Air heater and inlet air filter system | Electrical heater | 90 kW | Xianfeng |
|  | Cover | SUS304 | Xianfeng |
|  | Primary ,middle filter and HEPA | Screen 、non-woven fabrics， | Xianfeng |
| Inlet air and exhaust air system | Draught fan (separated installed with main machine) | （1）manual operation wind volume； （2）Motor power 30 Kw | Buy from market |
|  | Silencer | noise≤80 decibel, Carbon steel | Xianfeng |
|  | Inlet air duct with inlet air flap | SUS304 δ=2 mm | Xianfeng |
|  | Exhaust duct | SUS304 δ=1.5mm |  |
|  | Outlet air duct | duct：carbon steel δ=1.5mm | Xianfeng |
| Control system | Control cabinet | Stainless Steel | Xianfeng |
|  | Main electrical parts | Electric relay ,air switch and so on | Siemens |
|  | Indicating instrument | Ampere meter, voltmeter, temp sensor | Buy from market |
|  | Pneumatic element | cylinder、manifold block 、barometer | Buy from market |
|  | PLC |  | Siemens |
|  | Touch screen |  | Siemens |
| Bag filter |  | With antistatic fibre, uniformity release static electricity，no spark appear ，safety in production | Xianfeng |
| Viewing window | Toughened glass | Observe inside material condition | Xianfeng |

Spare Parts

| No | Name | Type | Unit | Qty |
| --- | --- | --- | --- | --- |
| 1 | Sealing strip |  | set | 1 |
| 2 | Compressed air tube | Ф10 | meter | 10 |

FLUIDIZED BED DRYER

GFG-300 FLUIDIZED BED DRYER

Technical Parameters：

| Item | Unit | parameter |
| --- | --- | --- |
| Feeding capacity | kg/batch | 200-300 |
| Fan power | KW | 30 |
| Consumption of steam | kg/h | 400 |
| Consumption of compressed air | M3/min | 0.9 |

Equipment list：

| name | details | Material and instruction | Manufacturer |
| --- | --- | --- | --- |
| Main frame system | Filter room: has the filters and the explosion release | SUS304 It fits for different kinds of powder and granule drying. | Xianfeng |
|  | Middle room: has view glass |  |  |
|  | One trolley: material flow in fluid-bed with stir motor |  |  |
|  | Lifting: double cylinder and air cell pressure |  |  |
|  | Air inlet room; it has water exit, adjustment air valve |  |  |
|  | Main tower support: cover with Sus304 |  |  |
|  | Main tower airproof: Silicon rubber |  |  |
|  | Temperature test: air inlet and air outlet |  |  |
| Air Heating system | Gas furnace |  | Xianfeng |
| Air Filtrating system | Initial and middle efficient filter | Sieve screen, none woven fabric | Xianfeng |
|  | Shell | SUS304 |  |
|  | Sub-high efficient filter | Three grade filter, meet 300000 level. |  |
| Air exhaust system | Suction fan | (1) hand adjustment air valve (2) engine power 30 Kw | Buy from market |
|  | silencer | Carbon painted, make sure the fan is closed off. noise≤80db(A) | Xianfeng |
|  | Air pipe | Pipes: sus304 |  |
|  | Dust exhaust pipe | Pipes: sus304 Flange: sus304 |  |
|  | Air exhaust pipe | Pipes: carbon steel Flange: carbon steel |  |
| Control system | Tank | Carbon steel plastic painted |  |
|  | Operation system | Touch screen control | SIEMENS |
|  | program | PLC |  |
|  | Electrical element | Touch, relay, button, air switch | SIEMENS |
|  | Indication instrument | Current watch, voltage watch, temperature sensor, temperature control |  |
|  | Air pressure element | Cylinder, air pressure watch |  |
| Hop pocket |  | Has anti static fiber, release the static equality, no fire. Safe produce. | Xianfeng |
| View window | glass | It can see the material in the machine | Xianfeng |

Spare parts：

| no | Name | Specification | Unit | qty |
| --- | --- | --- | --- | --- |
| 1 | Air cell | Supply as the machine | pc | 1 |
| 2 | Sealing strip of the main tower | Supply as the machine | set | 1 |
| 3 | Air compress pipe | Supply as the machine | m | 10 |

Quotation：

| No | Equipment | Model | Qty | Price (USD) |
| --- | --- | --- | --- | --- |
| 1 | Fluid bed granulator | FL-300 | 1 set | 42800 |
| 2 | Fluidized bed dryer | GFG-300 | 1 set | 38800 |
| FOB (Shanghai) | 81600 |

T/T: 30% deposit after signed contract, 70% balance before delivery.

Safety features：

The machines can’t be started without safe earthing.

The machines can’t be started without the bag filter not in place

The machines will stop with the bag filter leak

The machines will stop with explosive

The machines can’t be started without the inlet and outlet flap open

Documentation：

One copy of operational manual in English will be given with the delivery of machine.

Provide relevant certificates (such as product certificate, spare part certificate)

Provide additional set for spare part.

All our machines guaranteed for trouble free performance for a period of 12 months from commissioning.

Delivery date：

Within 45 work days

Packing：

Wooden case (Approved by custom)

After-sell service：

Installation and after-sell service free for one year. But the Buyer shall bear all the expenses incurred in the trip of the Seller's delegation for erection, commissioning and training, including air tickets, meal, hotel accommodation and local transportation.

We accept FAT for client.

Angela Xie

Jiangsu Xianfeng Drying Engineering Co.,Ltd

Add：Zhenglu industrial zone, Changzhou City, Jiangsu province, China

P.C.:213111                      http://www.czxf.cn/en/

FAX: 0086-519-88930288       Foreign trade: 0086-519-88930111

E-mail: 2005@czxf.cn