| Type | Steel | Aluminum Alloy |
| --- | --- | --- |
| Rated load | kg | 800（ including the weight of personnel ） | 800（ including the weight of personnel ） |
| Lifting speed | m/min | 8.2±0.5 | 8.2±0.5 |
| Dimension of platform (length×width×height) | mm | (2500+2500+900+900)×690×1180 | (2500+2500+900+900)×690×1180 |
| Suspension Mechanism | protrusion of front Beam | mm | 1300 | 1300 |
|  | Height of Front Beam | mm | 1150~1650 （ adjustable distance 100） | 1150~1650 （ adjustable distance 100） |
| Hoist | Type |  | LTD8.0 | LTD8.0 |
|  | Quantity | piece | 2 | 2 |
|  | Motor | Type |  | YEJ90L-4 | YEJ90L-4 |
|  |  | Power | kW | 1.8 | 1.8 |
|  |  | Voltage | V | 440 |
|  |  | Rotation Speed | r/min | 1400 | 1400 |
|  |  | Brake Torque | N-m | 15 | 15 |
| Safety Lock | Type |  | LSG20 | LSG20 |
|  | Quantity | piece | 2 | 2 |
|  | Allowable Impulsive Force | kN | 20 | 20 |
| Electric control box |  | Main parts in the control panel is schneider except the transformer |
| Weight | Platform | kg | 286 | 192 |
|  | Hoist | kg | 52.5×2 | 52.5×2 |
|  | Safety Lock | kg | 5.5×2 | 5.5×2 |
|  | Suspension Mechanism | kg | （ no-including Counter weight ）324 | 324 |
|  | Electric Control Box | kg | 15 | 15 |
|  | Counterweight | kg | 1000（25×40pcs） | 1000（25×40pcs） |
| Wire Rope | Type |  | 4×31Fi+PP-Φ8.3 Break Strength ≥70000N | 4×31Fi+PP-Φ8.3 Break Strength ≥70000N |
| Power Cable | Type |  | 3×2.5+2×1.5YC-5 | 3×2.5+2×1.5YC-5 |

Major technical data of

ZLP800