Gaoyuan SG always insists on the combination of innovation technologies and practical constructions. Its products spread more than 30 provinces all over China and 30 countries overseas in the America, Africa, Asia, Europe and Oceania, and are generally applied to functional layers constructions of newly built roads, maintenance projects, pavement inspections, road materials test and inspection, and so on.

Gaoyuan SG is the best maintenance equipments manufacturer in China with richest experience in domestic construction and technical research. With an excellent design team and production personnel, relying on the strong strengths of National Highway Maintenance Equipment Engineering Lab, Sino-Belarusian Road Engineering Institute, High Grade Maintenance Engineering Institute of Henan Province and Road Maintenance Engineering Institute of Xi’an City, Gaoyuan SG has been developing and releasing automatic asphalt distributors, micro surfacing paver and slurry seal equipment, chip seal equipment, fiber seal equipment, cold-recycling mixing equipment, multiple purpose maintenance equipment and so on.

Road Maintenance and Construction Equipment

HGY5314TFC Synchronous Chip Sealer

| Chassis model | HOWO, ZZ3317N4667D1 |
| --- | --- |
| Spray width | 3800 mm |
| Spray volume | 0.2-3.0 kg/m2 |
| Aggregates size | 3-25 mm |
| Asphalt tank | 8 m3 |
| Aggregates hopper | 14 m3 |
| Heater | Imported diesel heater(2×10×104kCal/h) |
| Spray medium | Hot (modified) asphalt, cutback, emulsion |
| Gross Vehicle Weight | 31000 kg |
| Dimensions | 11950×2500×3860 mm |

YXKT0812 Fiber Chip Sealer

| Auxiliary engine power | 70kw |
| --- | --- |
| Spray width | 3500mm |
| Spray volume | 0.5-3.0kg/m2 |
| Aggregates size | 3-25mm |
| Asphalt tank | 8m3 |
| Aggregates hopper | 12m3 |
| Heater | Imported diesel heater(2×10×104kCal/h) |
| Spray medium | Hot (modified) asphalt, cutback, emulsion |
| Length of fiber | 30/60/120mm |
| Fiber spray volume | 30-90/m2 |
| Full load weight | 50000kg |
| Dimensions | 12150×2500×4000 mm |

HGY5255GLQ Automatic Asphalt Distributor

| Chassis model | ZZ1257M4647D1 |
| --- | --- |
| Asphalt spray width | 200-6000 mm |
| Spray Amount | 0.2-3.0 kg/ m2 |
| Asphalt tank volume | 13000 L |
| Heater | Imported diesel heater(20×104kCal/h) |
| Spray Media | Hot (modified) asphalt, cutback, emulsion |
| Spray accuracy | ±1% |
| Gross Vehicle Weight | 25000 kg |
| Dimensions | 10735×2496×3820 mm |

GYRY06H Asphalt Emulsion Plant

| Max capacitance | 30kW |
| --- | --- |
| Colloid mill speed | 2900rpm |
| Colloid mill | 15 kW |
| HTF electrical heating power | 9kW |
| Burner heat capacity | 10×104 kCal/h |
| Heat exchanger area | 15 m2 |
| Emulsion fineness | <5μm |
| Productivity | 6 t/h |
| Weight | 4500 kg |
| Dimensions | 4700×2150×2330 mm |

HGY5311TFC Slurry Paver

| Chassis model | ZZ1317M3867D1 |
| --- | --- |
| Auxiliary Engine | 110kW/2300rpm |
| Aggregates hopper | 12 m3 |
| Emulsion tank | 4 m3 |
| Water tank | 4 m3 |
| Additive tank | 600 L |
| Filler tank | 2×0.5 m3 |
| Mixer discharging volume | Max.3.5 T/min |
| Min. vehicle speed | 1 km/h |
| Paving depth | 3-15mm |
| Spreader width | 2.5-4.3 m |
| Gross Vehicle Weight | 31000 kg |
| Dimensions | 11690×2496×3490 mm |