Circular Double-sided Printing Bag-making Machine

This machine, matched with laminating machine or not, is used for making laminated cement bag and various kinds of laminated PP woven bags.

It has the functions of printing, perforating, gusseting, flat-cutting, 7-type cutting, pneumatic-hydraulic auto edge correction for material feeding and has the advantages of high production efficiency, reasonable structure, easy maintenance and perfect printing.

It is the ideal equipment for making laminated bags and cement bags.

| Model No. | YF-ZD/A |
| --- | --- |
| Max. Input Width (mm) | 750 |
| Max. Printing Width (mm) | 600 |
| Bag Making Length (mm) | ≤ 1200 |
| Bag Making Width (after edges folded) (mm) | 300-500(600) |
| Output (pcs/min) | 60-150 |
| Double-side Printing Colors | 1-4(6) |
| Power of Motor (kw) | 4 |
| Drying Power (kw) | 10 |
| Fold Form | displacement or not |
| Error of Edges Folded | ≤ 3mm |
| Installing Dimensions (L×W×H) (mm) | 10300×1600×2200 |
| Approx. Weight (kg) | 5500 |