CIL-MFT-21C Full-automatic high-speed counting handkerchief folding machine production line (include full-automatic single-bag packing machine)

CIL-MFT-21C 全自动手帕纸折叠包装生产线（包含全自动手帕纸单包机）

This production line composed of handkerchief counting automatic folding machine and full-automatic handkerchief packing machine.

该生产线由两台机器组成。手帕纸生产机器和单包机器。

Description:

CIL-MFT-21C Mini type facial tissue machine adopts vacuum adsorb and high-speed to fold the paper. Adopting step-less adjusting speed, and it is running smoothly. It is special equipment for 4 folding facial tissue machine. This machine composed of raw paper stand, embossing unit, lengthways folding unit , cutting and transversal folding unit, It runs a whole set of rolling to fix difference tension of raw paper, embossed, lenghtways folding, pushing the paper, cutting the paper, transversal folding paper and finished products transfer.

产品论术

CIL-MFT-21C迷你型全自动手帕纸机采用真空吸附，高速自动叠纸。本机制造精度高，无级调速，动作准确，是四折叠面纸巾的专用设备,本机主要由原纸放卷装置,压纹装置,纵向折叠装置,切纸及横向折叠组成。生产流程是:放卷—→压纹—→纵向折叠—→拉纸—→切纸—→横向折叠—→成品挤送。

Features：

1.. Embossing design on raw paper with clear embossing shape.

2. Controlled with rolling tension to fit production with different tension of raw paper.

3. Mill edge infolding, the appearance of product is elegant.

4. Adopting screw turning knife to cut for easy adjustment

5. Adopting vacuum folding format.

6. Equipped with single color or double color printing according to customers’ requirement.

功能与特点：

1、纸面辗轧花纹，图案明显清晰。

2、放卷张力控制，适应不同张力原纸生产。

3、纸边内折，产品外观雅致。

4、螺旋刀体，剪切轻快，调整简单。

5、采用真空折叠形式。

6根据用户需求，可配装单色或双色印刷装置。

Technical Parameter for handkerchief counting automatic folding machine:

1、Designed speed: 800 pcs/min
2、Stable production: 500-600 pcs/min.

3、Power of main machine :5.5KW
4、Power of blower:5.5kw
5、Air pressure:≥0.6mpa
6、Final product specification（LxW mm）
   a.75x52 (opening 210x210)  mini type
   b.105x52 (opening 210x210) standard type
7、Weight: about 1.3T

技术参数：手帕纸机

1、设计速度：: 800 片/分钟
2、稳定速度: 500-600 片/分钟.

3、主机功率 :5.5KW
4、风机功率r:5.5kw
5、气压:≥0.6mpa
6、成品规格（长x宽 mm）
   a.75x52 (展开 210x210)  迷你型
   b.105x52 (展开 210x210) 标准型
7、重量: 大约1.3T

Technical Parameter for: full-automatic handkerchief packing machine

1、Packing size:  Standard type : 106mm╳53mm╳26mm     10 sheets

Mini type     72 mm╳53mm╳26mm      10 sheets

2、Dimension of packing film: Standard type 150mm

Mini type    116mm

3、Speed (bags/min): 25~90

4、Overall size: 2840 mm╳2650 mm╳1720 mm

5、Power of motor: Main motor:1.1 kw

Power of motor for output side sealing: 0.18kw

Heating power: 3.4kw

6、Power supply: 380V 50HZ

7、Air pressure: 0.3~0.4mpa

8、Weight of machine: about 1500KG.

技术参数：全自动手帕纸单包机

1、产品尺寸:  标准型 : 106mm╳53mm╳26mm     10 片

迷你型： 72 mm╳53mm╳26mm     10 片

2、包装膜的规格: 标准型 150mm

迷你型 116mm

3、包装速度 (包/分钟): 25~90

4、机器尺寸: 2840 mm╳2650 mm╳1720 mm

5、功率: 主机:1.1 kw

外封: 0.18kw

加热: 3.4kw

6、电源: 380V 50HZ

7、气压: 0.3~0.4mpa

8、重量: 1500KG.