Oil-free Little Cam Four-shuttle Circular Loom

1. Small cam type and convex table as well as swing-beam rolling wheel transmission is adopted, making it easy and stable to run.
2. Slide block and rod are eliminated while the wearing parts are decreased. Rolling transmission is adopted in entire structure, which doesn't need lubricant.
3. Frequency speed regulation which is convenient and stable is adopted.
4. It is configured with automatically stop detecting unit when meeting the situation of warp/weft breaking, weft ending. The stoppage unit is sensitive and reliable.
5. It's an environmental product whose noise is not more than 80dB(A).
6. Low strength plastic yarn which is made from 100% regenerated plastic can be adopted to weave.
7. It is high-efficient and energy-efficient. The highest rotation speed of the main motor can reach 180r/min and the power is 1.5/2.2kw, which can save 10 thousand degree electricity compared with the traditional four shuttle circular loom whose power is 4kw.
8. It is a patent device. (Patent No.: ZL 200820166333.1)

Main Technical Parameters:

| Model No. | YF-BT/BC-750/4 |
| --- | --- |
| Number of Shuttle | 4 |
| Folding Width of Weaving (mm) | 350-750 |
| Max. Number of Warp | 640/768 |
| Rotational Speed of Main Body (r/min) | 140-180 |
| Production Capability (m/min) (40 warps /100mm)) | 1.4-1.8 |
| Power of Main Motor (kw) | 1.5-2.2 |
| Gross Power of Motor (kw) | 2/2.7 |
| Approx. Weight (kg) | 1800 |
| Installing Dimensions (L×W×H) (mm) | 8300×2200×2730 |
| Unite Price(FOB Wenzhou) | USD5200.00 |

Remarks:

Country of Supply/Origin: China

Type of Packing: Packed in nude

Warranty Period: One year except quick-wear parts.

Term of Payment: 30%T/T as the advance, 70%T/T before the delivery.

Delivery Period: Within 30~40 days after we receive the advance payment or L/C

Installation: The buyer provide each technician the accommodation, the round-trip ticket, visa and salary $65/person/day.