Relief offset printing machine

This machine is used for printing letters, figures and trademarks on plastic woven bags with two or three color chromatography. This assembly goes with automatic counting and flashed fine turning and does automatic printing with photocell control.

Main Technical Parameters:

| Item No. | Max input width(mm) | Max printing width(mm) | Max printing length(mm) | Thickness of rubber relief printing plate(mm) | Diameter of pring roller(mm) | Printing capacity(pcs/h) | Number of printing color |
| --- | --- | --- | --- | --- | --- | --- | --- |
| S-YFY-800IIIB | 800 | 660 | 1200 | 4 | 480 | 1000-2000 | 4+0 |
| Power of motor(kw) | Installing dimentions (mm) | Weight (kg) | Price |  |  |  |  |
| 2.2 | 3400*1400*1300 | 2000 | $6120 |  |  |  |  |

Flexographic Printing Machine

Main Technical Parameters:

| Type | Max diameter of unwinding roll | Max.width of unwinding roll | Max.printing width | Printing length | Max printing colors | Printing speed | Gross power |
| --- | --- | --- | --- | --- | --- | --- | --- |
| YF-RY4800 | 1200mm | 800mm | 700mm | 230-1200mm | 4 | 5-50m/min | 12kw |
| Weight | Installing dimensions | Price |  |  |  |  |  |
| 3500kg | 6*1.8*2.4m | $17,800 |  |  |  |  |  |