Model  DFJ-500 DISPOSABLE GLOVE Making Machine

The  disposable  glove  machine is an ideal equipment for batch production of PE, EVA and CPE film gloves. it has such advantages as stable product quality, automatic control, easy to operate and maintenance. The main power of the machine adopts 1.5KW,220V Panasonic frequency converter  with stable performance and low noise. The control part is equipped with single chip microcomputer control, and step motor with low maintenance rate and low noise.

| Model | DFJ-500 |
| --- | --- |
| Producing Length | 200-400mm |
| Producing width | 270-330mm |
| Film thickness | 0.008-0.02mm |
| Producing Speed | 40-130pcs/m |
| Main Power | 1.1Kw |
| Power Source | 220V 50HZ |
| Weight | 600Kg |
| Overall dimensions(L*W*H) | 2300*1190*1500mm |

| Item | Model | FOB NINGBO Price(US/$) | Qty/set | Amount |
| --- | --- | --- | --- | --- |
|  |  |  |  | (US/$) |
| Model DFJ-500 DISPOSABLE GLOVE Making Machine | DFJ-500 | $8,000 | 1 | $8,000 |
|  |  | Total: | 1 | $8,000 |

1).Price term: FOBNINGBO PRICE.

2).Payment: 30% down payment of the total value in the contract should be paid by T/T to the Seller as deposit, the balance 70% of the total value should be paid by T/T  before shipment. when goods is ready.

3).Delivery time: Within 20-35working days after receipt of advance.

4).Packaging: Plastic film

5) Guarantee: one year

6).Minimum order: 1 set

7).Validity of price: 3 months

8）The seller agree to send one engineer to Buyer's factory for installation as requested by the Buyer, but all expenses shall be borne by the Buyer such as VISA， air ticket, hotel and food charge, after installation, the Buyer should pay the engineer 80 USD/day as subsidy.