ABOUT US

- COMPANY INTRODUCTION

Founded in the early 1980s as one of the few state-authorized packing machinery enterprises, and re-founded as a private company in 2000. Shanghai Zhonghe Packing Machinery Co., Ltd. Specializes in designing and manufacturing different kinds of automatic packing machines and has developed more than 80 different models, which are well applied in the food, chemical, pharmaceutical, and light industries, etc.

Based on the solid home market, Shanghai Zhonghe Packing Machinery Co., Ltd. is now gradually promoting the international market with effective and efficient sales and after sales services.

Shanghai Zhonghe Packing Machinery Co., Ltd. will continually be innovative and updating its service in all aspects to ensure that the machines are worth the trust of customers all over the world.

DCF-240 POWDER PACKING MACHINE

This series installed powder auger dosing system.can pack powder products such as milk powder, medicine and chemicals powder, etc.

Features

- Bag-making, measuring, filling, sealing, cutting and counting are all finished automatically.

2. Either under set length control or photo-electronic color tracing, we set bag length and cut in one step. Time and film saving.

3. The temperature is under independent PID control, more suitable for different packing materials.

4. The driving system is simple and reliable, and maintenance is easy.

5. Applicable material should be composite films like: PET/PE, Paper/PE, PET/AL/PE, OPP/PE.

MACHINE PICTURE

Technical Specification (FOB port Shanghai in US$)

| Item | Description of Item | Unit Price | Qty. | Total Price |
| --- | --- | --- | --- | --- |
|  |  | in USD |  | in USD |
| 1 | Machine | Automatic Powder Packing Machine | 6000 | 1 | 6000 |
|  | Model | DCF-240 (max film width to be 200mm through change different bag former ) |  |  |  |
|  | Sealing type | 4-side sealing |  |  |  |
|  | Measurement | Auger type (1-2g，2-10g and 10-30g through change auger set) |  |  |  |
|  | Cutting type | Rotary straight cutter with tear notch |  |  |  |
|  | Sealer | Horizontal and Vertical sealer: diamond |  |  |  |
|  | Packing speed | 40 - 60bag/min （Depend on Products） |  |  |  |
|  | Bag size | W:40-100mm L:50-130mm |  |  |  |
|  | Total power | 2150W |  |  |  |
|  | Voltage | 220V or 380V |  |  |  |
|  | Machine Net Weight | 200Kg |  |  |  |
|  | Mainframe Dimensions | L×W×H： (625x751x1558)mm |  |  |  |
|  | Material | Stainless steel 304 |  |  |  |
|  | Includes | Inverter, photo sensor, short output belt conveyor,ribbon printer, a vibrator, one bag former and one auger set |  |  |  |
| 2 | Optional | Touch parts: stainless steel 316L | 1000 | 1 | 1000 |
|  |  | Additional bag former ss304 | 60 | 1 | 60 |
|  |  | Additional bag former ss316 | 100 | 1 | 100 |
|  |  | Additional auger set ss304 | 300 | 1 | 300 |
|  |  | Additional auger set ss316 | 420 | 1 | 420 |

Installation and debugging: Finish installation and debugging before shipping. Buyer pay all the business fee including VISA application, traffic, hotel and resturant and pay mission allowance US$50 everyday each person if need local installation and debugging.

Guarantee: One year from the date of shipment against any manufacturing defects

Shipment: Within 15 or 25 working days from receiving 30% deposit

Payment:T/T, 30% deposit in advance and full payment before delivery

DETAILS PICTURES AS BELOW

- Bag former (different shape with different bag former, 4-side sealing refer to middle one)

- Powder dosing system - auger kind

It is volume way not weigh.  Press FUNTION botton, reach Fill through ▲ or ▼ to change fill amount then get different weight.

- Date coding ribbon printer

Tool box (includes free part, free tools and doc)

- Free part with Machine

| Item | Description of Item | Qty. |
| --- | --- | --- |
| 01 | Gum over (fix the film etc) | 02 |
| 02 | Solid relay | 01 |
| 03 | Heat pipe | 04 |
| 04 | Thermocouple | 02 |
| 05 | Proximity switch | 01 |
| 06 | Ribbon(match machine) length:100m | 01 |
| 07 | Fuse(set) | 01 |
| 08 | Zigzag cutter | 01 |

- Free tooling with Machine

| Name | Spec | QTY |
| --- | --- | --- |
| socket head wrench | STD | 1set |
| cross screwdriver |  | 1Pc |
| straight screwdriver |  | 1Pc |
| screwdriver |  | 1Pc |
| scissors |  | 1Pc |
| copper brush |  | 1Pc |
| hairbrush |  | 1Pc |
| Toolbox |  | 1Pc |

- Doc with Machine

| Name | Spec | QTY |
| --- | --- | --- |
| Manual | According to ordered machine | 1 |
| Frequency conversion manual |  | 1 |
| Temperature controller Manual |  | 1 |
| Proxmity switch Manual |  | 1 |

# Text boxes

Features

1. heating code printer

2. three lanes

3. each lane can put 13 codes (each code W2mm H3mm)

4. easy to change codes (0-9, A-Z)

5. Use ribbon, each roll 100m

4-side sealing sample bag