雁峰集团有限公司

# YANFENG GROUP CO., LTD.

ADD: PINGYANG ECONOMIC DEVELOPMENT ZONE, ZHEJIANG, CHINA.

TEL: +86-577-63032858 / 63032878             FAX: +86-577-63032868

E-mail: jessica@yanfeng.cn Website: http://www.yanfeng.cn

Rotary Die Film Blowing Machine

Model:SJ-60/FM1000

- Screw Diameter:60mm

- L/D Rotio of Screw:28:1

- Screw Speed:10-100r/min

- Max Output:65kg/h

- Power of Main Motor:18.5kw

- Specification of Die Head:￠100-180

- Rotaional Mode of Machine Head:Continous Rotaion

- Single-side Thickness of Film:0.01-0.1

- Max.Folding Width of Film:1000mm (two layer 1000mm,add a knife on film side,and it will become one layer film,width 2000mm)

- Groww Power:30kw

- Weight of Machine:3000kg

- Overall Dimension:6.5*2.2*4.5m

- FOB Wenzhou Price :$15000

Recycling Machine

Model:SJ-FL150/120

- Main screw ￠150mm ,length 1500mm,L/D ratio 10:1

- Sub screw ￠120mm,length 1200mm, L/D ratio 10:1

- Rotaional speed:50-80r/min

- Power of motor:37kw

- Power of sub-motor:11kw

- Heating power:30kw

- Production capacity: 120kg/h

- Electric Components:Made in Wenzhou

- Screw Material:No.45 Steel

- Pelletizing Kife:High speed steel cutter

- System changerhead:Manual

- FOB Wenzhou Price :$9200