RT700C  Bag Making Machine with Zipper Attachment

Delivery time: 50 days

Packing: on wooden pallet and wrapped with stretched film

Payment: 30% T/T as deposit, balance 70% after inspect machine at our factory

Installing cost: the buyer need to pay the visa, the round air ticket, hotel, food, traffic and salary 100USD/day for technician.

PS: The quotation is effective in 15 days.

Usage:

- RT-700C Bag making machine with zipper attachment is a multi-functional bonding bag making machine, having been improved on the base of RT700B.

- It is produced by our company through modifying, rectifying and testing based on advanced technology from home and abroad.

- This machine is specially equipped to JL 45 Zipper extruder in order to make different kinds of plastic zipper bag (zip lock bag, slider zipper bag, grape bags and so on).

- This machine can settle some difficulties that the traditional way of making zip lock bag encountered, such as the multi-color printing; the size of bag is limited by the die head, etc.

5.  This machine has functions of edge folding, bottom folding, thermal bonding, spots breaking, perforating, welding and scalding, hot cutting and sealing, etc.

Characteristics:

- Compared with RT700A, the front cutting bag part of RT700C is cutting on the silicon belt instead of cutting on the rubber covered roller, so it can strengthen the bag hot sealing, and beautify the sealing of the bags.

- This machine equips automatic stop equipment for running out of material, photocell error and temperature abnormality.

- Compared with RT700A and B, RT700C adopts horizontal type of attachment, it can improve the smoothness of the attachment (thermal bonding), and make the machine work more smoothly, easily and stably.

- Its transmission part has been changed to use swinging arm type transmission, which is the same as the three-sides sealing machine transfer motion, instead of eccentric drive transmission.

- The whole machine frame is welded by 14 mm entirety steel iron plate, instead of being welded by channel steel. (U-bar Welded)

- The cutting knife adopts steel plate bridge type beam, which makes the machine more stable and make the speed quicker.and easy to turn up and down and convenient to repair the knife.

- The transmission part of hot cutting knife has been changed to use the international standard type of steel shaft linear bearing bar，which can avoid the damage or deformation of the transmission chaining part because workers forget to add oil to the knife, so that can also improve the quality of making bag.

- It adopts advanced computer control system, LCD and drive and can break zip and film as well as automatically alarm and stop, and it applies functions of photoelectric deviation-rectifying, magnetic powder tension control to the process of edge folding.

- It adopts Japan Yaskawa Servo Motor, which guarantee to control the machine and make high quality bags.

- Main machine: Panasonic frequency converter

- Main motor: Famous brand in China.

- It adopts the reinforcing rib silicon conveyor belt: 5mm silica gel plate, in order to fit the zipper strip part of zip lock bags, during its production, the cotton thread (reinforcing rib) is added to improve belt’s firmness to make the bag cutting more neat and beautiful)

- It adopts the embossing aluminum pressing plate to seal the bag more firmly, neatly and beautiful.

- The bridge type knife beam, the pressing plate and the presser foot use No. 45 steel, all of them are produced by linear cutting.

- The plate under the silicon bet can go up and down, so it is easy for you to change the silicon belt.

- The spring of knife, the pressing plate and the presser foot are imported from Japan.

Main technical data:

| Model | RT-700C |
| --- | --- |
| Material | LDPE |
|  | PP ( change the cooper knife to iron knife) |
| Speed | 40-60 bags /minute ( zipper bags) |
|  | 40-150bags /minute (Side seal bag) |
| Width of bag | ≤650 mm |
| Length of bag | ≤630 mm |
| Thickness of film | One layer 0.03-0.07 mm |
| Power | 12.5 KW |
| Heater | 2.6 KW |
| Main motor | 2.2 KW |
| Air pressure | 4 HP |
| Estimated overall dimensions | 6800X1400X1850mm |

Wenzhou Xinda Zip Lock Bag Making Equipment CO.,LTD

Nora Shao

555 the second road ruian economic development zone,wenzhou city,zhejiang province,China.

Tel:86-577-65155000     Fax:86-577-65155080  Mob:86-15888200169

Email:huiye402606@yahoo.cn

MSN:huiye402606@live.cn

ADD：555 the second road ruian economic development zone,wenzhou city,zhejiang province,China    http://www.xindamachine.cn

TEL：86-577-65155000　65155077   FAX：86-577-65155080           E-mail：nora1176@xindamachine.com