#### 浙江建达机械有限公司

ZHEJIANG JIANDA MACHINERY CO.,LTD

Tel:0086-577-65159968  Fax:0086-65599887  contact person: Ms Sunny

地址：浙江省瑞安经济开发区港口大道399号 (邮编：325200)

Address: #399 Gangkou Road, Ruian industrial area, Wenzhou city, Zhejiang China

Website: http://www.jiandajx.com        Email:jd@jiandajx.com

PLASTIC CUP COMPLETE PRODUCTION LINE (total 9 pages)

Project name: plastic cup production line

Machine equipment:

Item1: JDSP-105 PLASTIC SHEET EXTRUDER

Item2: JD-660B PLASTIC CUP THERMOFORMING MACHINE

Item3: MOULD

Item4: COMPRESSOR

Item5: JDP-720 CUP STACKING MACHINE

Item6: JD-800 CRUSHER

Item7: JDM-1000 MIXER

Item8: JDQL-15FA Chiller

| NO. | MACHINE | MODEL | UNIT PRICE |
| --- | --- | --- | --- |
| 1 | plastic sheet extruder | JDSP-105 | 31,000USD/SET |
| 2 | plastic cup thermoforming m/c | JD-660B | 21,600USD/SET |
| 3 | Cup mould | real price fixed as per your sample | 3,850USD/SET (round cup price) 5,000 USD/SET (square tray price) |
| 4 | Screw type compressor | 3 cubic | 5,200USD/SET |
| 5 | Cup stacking machine (only suit for cup not for tray) | JDP-720 | 4,300USD/SET |
| 6 | Crusher | JDG-800 | 2,700USD/SET |
| 7 | mixer | JDM-1000 | 1,000USD/SET |
| 8 | Chiller | JDQL-15FA | 5,500USD/SET |

Price list based on FOB ningbo, China:

- item1: JDSP-105 PLASTIC SHEET EXTRUDER

Short video link: http://en1.jiandajx.com/about7shows_14.html

#### I. General

This machine is designed to produce plastic sheet for thermoforming/vacuum forming purpose or stationery use, which is composed of 7 parts – extruder part, filter part, Die-head part, 3 rollers part, traction part, winding part and side trimming part.

#### II.Major Specification

### Machine name: plastic sheet extrusion line

Model No.: JDSP-105

Applicable Material: PP (polypropylene) or PS (polystyrene). If use PS material, should add 3 thermostat on the cooling roller, which is extra pay.

- EXTRUDER PART: 01 set

Hopper: 1 set

Output: 125kg/h

Screw dia.: Ф105

L/D: 30:1

Screw & barrel material: 38 CrMoAlA after nitrogen treatment with optimum hardness, strong corrosion resistance and long service lifetime

Screw rotate speed: 0-70r.p/min

Speed adjustment: Frequency inverter

Drive motor power: 37.0kw

Heating way: aluminium-casted heater

Heating power: 30.0kw

Gear box: hard-toothed

2.  FILTER PART: 01 set

Worm-gear case: 1 pc

Filter size: 200mm x 40 mm

Net dia.: Ф3-3.5mm

Heating power: 5kw

net change: by motor changing/replacement

Limit switch/board: 1pc

3. DIE HEAD PART: 01 set

sheet structure: 1 layer

T-die design: like cloth-hanger, enable the melting material be flowed evenly from the outlet.

Die head Width: 750mm

Finished sheet width: 660mm

sheet thickness: 0.3-1.5mm

Heating way: Aluminum-casted heater

4. 3 ROLLERS PART: 01 set

Roller dia.: 300mm

Roller length: 750mm

Roller no.: 3 pcs

Rollers reach to “mirror surface” standard

3 rollers layout: inclined

Roller linear speed: 0-13m/min

Driving motor: 4.0kw

Roller part movement: by motor, 1.1kw

5. TRACTION PART: 01 set

Traction roller dia.: Ф160mm

Traction roller length: 750mm

Traction motor power: 2.2kw

Speed adjustment: frequency inverter

Cooling roller dia.: Ф65mm

- WINDING PART: 01 set

Winding rubber roller: 1 pc

Flat roller: 1 pc

winding motor power: 1.5kw

finished roll max.dia.: 710mm

7. SIDE TRIMMING PART: 01 set

Trimming knife: 2 pcs

Bracket traction length: 2.8m

8. OTHERS

Machine size: 12.0mx3.8mx2.2m

Machine weight: 11.0T

Power supply: 380v/3phase/4lines/50hz

- Item2: JD660B PLASTIC CUP THERMOFORMING MACHINE:

#### I. General

This machine is a kind of efficient automatic plastic thermoforming equipment developed and manufactured according to plastic thermoforming technical process. It can finish producing product at one time through sheet feeding, heating, stretching, forming and side cutting etc. It can produce such as PP, PS and ABS,etc. This equipment adopts microcomputer control with semiautomatic and automatic functions. This machine has sun advantages as wide us, stable running and smooth operation, high rate of finished products and low noise, etc.

#### II.Major Specification

Sheet width: 500-660mm

Sheet thickness: 0.2-1.5mm

Max. Forming Area: 640×240mm

Max. Forming Depth: 120mm

Max. Diameter of Sheet Roll: 700mm

Main Motor Power: 7.5kw

Winder Motor: 0.55kw

Heating Power: 64kw

Sheet Feeding Motor: 2.2kw

Working Gas Pressure: 0.7Mpa

Capacity: 20-35cycles/min

Dimension: 3500×1500×2700mm

Weight: 4.2T

Power Supply: 380/3/4/50(Volt/Ph/Line/Hz)

- Item3: Mould

Picture is as above. The mould cavity and real price depends on the client’s sample.

- Item 4: SCREW TYPE AIR COMPRESSOR

I. technical parameters:

Volume flux: 3.0m³/m

Air pressure: 0.8Mpa

Axis power: 18.5kw

- Item 5: JDP-720 AUTOMATIC CUP STACKING MACHINE:(ONLY FOR ROUND CUP NOT FOR SQUARE TRAY)

- technical parameters:

Cup dia: ￠61-67mm

Cup height: 75-110mm

Output: 20,000pcs/h

Total power: 0.65kw

Machine size: 4200mm×1100mm×1560mm

Machine weight: 1.0T

- Item 6: JDG-800 Crusher

I. technical parameters

1.motor power: 15kw

2.size: 1.5×1.2×1.85(m)

3. weight: 1.0T

- Item7: JDM-1000 Mixer

I. technical parameters

1. dia: ￠1000mm

2.motor power: 1.1kw

3.size: 1.0×1.0×1.2(m)

4.weight: 0.3T

- Item 8: JDQL-15FA Chiller

I. technical parameters:

Cooling capacity: 25000 kcal/h

Input power: 8.4 kw

Air cooler: 0.25*2 kw

Refrigerant: R22 (404A)

Cistern storage: 136L

Chilled water flow: 75L/min

Ambient temperature: No more than 40 degree

Water in & out temperature: 5-45 degree

Chilled water outlet & inlet: 1”

Overall size: 1250*760*1450

COMMERCIAL TERMS:

Article 1. Terms of payment

-------30% of the total value shall be paid by T/T in advance

-------the balance 70% of the total value shall be paid by T/T after inspection                             in the Seller’s Factory and before shipment

Article 2. Terms of payment

--------seaworthy packing by Stretch film and bubble film. Only electric   control box will be packed by wooden box.

Article3. Lead time

-------35 days after receiving the deposit

Article 4. Terms of gurantee

-------Periods of gurantee: 1 year

Article 5. Special Provisions

-------- The Seller agree to send one engineer to Buyer’s factory for installation as requested, but all expenses shall be borne by the Buyer such as air ticket , hotel and food charge, (in one week), after 7 days, the Buyer should pay the engineer 100 USD/day as subsidy.