#### 浙江建达机械有限公司

ZHEJIANG JIANDA MACHINERY CO.,LTD

Tel:0086-577-65159968  Fax:0086-65599887  contact person: Ms Sunny

地址：浙江省瑞安经济开发区港口大道399号 (邮编：325200)

Address: #399 Gangkou Road, Ruian industrial area, Wenzhou city, Zhejiang China

Website: http://www.jiandajx.com        Email:jd@jiandajx.com

Project name: plastic cup production line

| NO. | MACHINE | MODEL | UNIT PRICE |
| --- | --- | --- | --- |
| 1 | plastic sheet extruder | JDSP-105 | 31,000USD/SET |
| 2 | plastic cup thermoforming m/c | JD-660B | 21,600USD/SET |
| 3 | Cup mould | real price fixed as per your sample | 3,500USD/SET (round cup price) |
| 4 | Screw type compressor | 3 cubic | 5,200USD/SET |
| 5 | Cup stacking machine (only suit for cup not for tray) | JDP-720 | 4,500USD/SET |
| 6 | Crusher | JDG-800 | 2,700USD/SET |
| 7 | mixer | JDM-1000 | 1,000USD/SET |
| 8 | Chiller | JDQL-15FA | 5,500USD/SET |

Price list based on FOB ningbo, China:

- JDSP-105 PLASTIC SHEET EXTRUDER

Short video link: http://en1.jiandajx.com/about7shows_14.html

Technical data:

sheet width: 650mm

Sheet thickness: 0.3-1.5mm

Output: 125kg/h

Screw dia.: Ф105

Main motor power: 37kw

Total power: 92kw

Weight: 6000kg

Machine size: 10.5m*3.2m*2.7m

- JD660B PLASTIC CUP THERMOFORMING MACHINE:

Short video link: http://en1.jiandajx.com/about7shows_6.html

Technical data:

Sheet width: 500-660mm

Sheet thickness: 0.2-1.5mm

Max. Forming Area: 640×240mm

Max. Forming Depth: 120mm

Max. Diameter of Sheet Roll: 700mm

Main Motor Power: 7.5kw

Winder Motor: 0.55kw

Heating Power: 64kw

Sheet Feeding Motor: 2.2kw

Working Gas Pressure: 0.7Mpa

Capacity: 20-35cycles/min

Machine size: 3.5m×1.5m×2.7m

Weight: 4200kg

- Mould

The mould cavity and real price depends on the client’s sample.

(4) SCREW TYPE AIR COMPRESSOR

technical parameters:

Volume flux: 3.0m³/m

Air pressure: 0.8Mpa

Axis power: 18.5kw

(5) JDP-720 AUTOMATIC CUP STACKING MACHINE:(ONLY FOR ROUND CUP NOT FOR SQUARE TRAY)

technical parameters:

Cup dia: ￠61-67mm

Cup height: 75-110mm

Output: 20,000pcs/

Total power: 0.65kw

Machine size: 4200mm×1100mm×1560mm

Machine weight: 1.0T

(6)JDG-800 Crusher

technical parameters

1.motor power: 15kw

2.size: 1.5×1.2×1.85(m)

3. weight: 1.0T

(7)JDM-1000 Mixer

technical parameters

1. dia: ￠1000mm

2.motor power: 1.1kw

3.size: 1.0×1.0×1.2(m)

4.weight: 0.3T

(8) JDQL-15FA Chiller

technical parameters:

Cooling capacity: 25000 kcal/h

Input power: 8.4 kw

Air cooler: 0.25*2 kw

Refrigerant: R22 (404A)

Cistern storage: 136L

Chilled water flow: 75L/min

Water in & out temperature: 5-45 degree

machine size: 1.25m*0.76*1.45m