HQ-150 Plastic Grinding Milling Granulator

Main Features:

A: Milling, mixture and staining can be processed all in one

B: The machine takes up little area of land

C: It is characterized by simple structure and ease of operation

D: The interstitial of the blade can be adjusted with convenience of replacing.

E: It is characterized by high efficient in production and low consumption(1 ton of daily production ,and 200 degrees of electricity consumption ).

F: Granulate at lower temperature, do not damage molecular structure of materials basically, and do not damage physical performance.

Main Technical Variables:

| Capacity of Barrel | 150L |
| --- | --- |
| Output Capacity | 60-80kg/h |
| Main Motor Power | 18kw |
| Water Adding Device | 125w |
| Heating Power | 1.5kw |
| Rotary Speed of Main Shaft Weight of machine | 660r/min 1000kg |
| Overall Dimensions | 1500×700×1400mm |

| Item | Model | FOB Ningbo PRICE | Qty/set | Amount |
| --- | --- | --- | --- | --- |
|  |  |  |  | (US/$) |
| HQ-150 Plastic Grinding Milling Granulator | HQ-150 | $5,800 | 1 | $5,800 |
|  |  | Total: | 1 | $5,800 |

1).Trader terms: FOB Ningbo.

2).Payment: 30% of the total value of the contract should be paid by T/T to the Seller as deposit, the balance 70% of the total value should be paid by T/T  before shipment. when goods ready.

3).Minimum order: 1 set

4).Delivery time: Within7- 20days after receipt of advance.

5).Packaging: Plastic film.

6).Guarantee: one year

7).Validity of price: 3 months!

8).The seller agree to send one engineer to Buyer's factory for installation as requested by the Buyer, but all expenses shall be borne by the Buyer such as VISA, air ticket, hotel and food charge, (in one week),after 7 days, the Buyer should pay the engineer 80USD/day as subsidy.