Product: BP1000BP330 Block Concrete Batching Plant

| No. | Name | Description | Qty. | Remark |
| --- | --- | --- | --- | --- |
| Face Material Batching System |
| 1 | Planetary Mixer MP330 | Filling volume:500L; Compacted concrete per batch: 330L; Mixing power: 15KW; Pneumatic discharging; Two discharging doors; Reduction gearbox is specifically designed for a balanced distribution of power with low-noise rotation; One mixing star; One discharging scraper; One side scraper; Large maintenance gate allows easy access; Water spraying nozzles; Cr-hard cast iron blades and scrapers; Hardox liners and tiles; Emergency stop and security lock switch. Skip hopper, 500L; Reducer and motor, 3kw; Rail; Limit switch. Feeding ports for sand, cement and water. | 1 set |  |
| 2 | Batching System PLD800 (1 bin) | Aggregate storage bins: 1X6m³; Pneumatic discharging gate: 1 units; Cylinder, 1 units, ARTEC; Belt weighing system, 500L; B=500mm; Driving device, 5.5kw; Sweeping device; Tightening device; Belt scale unit; Filter net for sand; Vibrator for sand,0.25kw; Steel structure. | 1 set |  |
| 3 | Cement Scale CD330 | Weighing hopper, Max. weighing: 200kg; Load cells; Butterfly valve, VIFS200; Vibrator, 0.25kw; Framework. | 1 set |  |
| 4 | Water Weighing System WD330 | Turbine flow meter; Moisture probe, Origin from Germany Water pump; Pipeline and accessories. | 1 set |  |
| 5 | Screw Conveyor | SC168-9m | 1 set |  |
| 6 | Dust collector | Mixer dust collector | 1 set |  |
| Base Material Batching System |
| 7 | Planetary Mixer MP1000 | a. Filling volume:1500L; Compacted concrete per batch: 1000L; Mixing power: 37KW; Hydraulic discharging, 3kw; Two discharging doors; Reduction gearbox is specifically designed for a balanced distribution of power with low-noise rotation; Three mixing stars; Two discharging scrapers; One side scraper; Large maintenance gate allows easy access; Water spraying nozzles; Cr-hard cast iron blades and scrapers; Cast iron liners and tiles; Emergency stop and security lock switch. Skip hopper, 1600L; Reducer and motor, 11kw; Rail; Limit switch. Feeding ports for sand, cement and water. | 1 set |  |
| 8 | Batching System PLD1600 (4 bins) | a. Aggregate storage bins: 4X6m³; Pneumatic discharging gate: 4 units; Cylinder, 4 units, ARTEC; Belt weighing system, 1600L; B=650mm; Driving device, 11kw; Sweeping device; Tightening device; Belt scale unit; Filter net for sand; Vibrator for sand,0.25kw; Steel structure. | 1 set |  |
| 9 | Cement Scale CD1000 | a. Weighing hopper, Max. weighing: 500kg; Load cells; Butterfly valve, VIFS250; Vibrator, 0.25kw; Framework. | 1 set |  |
| 10 | Water Weighing System WD2000 | a. Turbine flow meter; Moisture probe, Origin from Germany Water pump; Pipeline and accessories. | 1 set |  |
| 11 | Screw Conveyor | SC219-9m | 1 set |  |
| 12 | Dust collector | Mixer dust collector | 1 set |  |
| Base Material and Face Material Shared Items |
| 13 | Water Supply System | Water tank, 2T; Water pump for MP1000 Water pump for MP330 Pipeline and accessories | 1 set |  |
| 14 | Pneumatic System | Air compressor, 1 unit; Triad(oil-water separator, reducing valve), fast joint and pneumatic elements; Storage tank. | 1 set |  |
| 15 | Electric Control Cabinet and Control System | Control cabinet Control panel for work flow; Dynamic display for work process; Industrial control computer 22’LCD Printer UPS Weighing meters Production software, in English; Air switch, relay, safety device, etc.; Wire, cable, bridge; Safe relay, safety protection in the cabinet; | 1 set |  |
| 16 | Steel Frame | Platform, discharging height, 5.0 m Guardrail, ladders, legs, etc. Concrete collecting hopper | 1 set |  |
| 17 | Cement Silo Accessories | a. Dust collector, 2*1 unit b. Level indicator, 2*2 units c. Air fluid gasket, 2*6 units c. Pressure safety valve, 2*1 unit | 1 set |  |