温州市益彰贸易有限公司

#### WENZHOU CHANGS INTERNATIONAL

ADD:#1105,Guoguang Mansion     发    票             No : 0808CHS14

(Opposite railway station

PROFORMA   INVOICE       DATE:108th august /2014

# WENZHOU CHINA

Tel:+86-577-86051848

ATTN: KACETE HOCINE

Tizi ouzou Algerie

| Number | Description &Specification | Quantity | Unit Price | Amount |
| --- | --- | --- | --- | --- |
|  | MULTILAYER KRAFT PAPER BAG MAKING MACHINE FL-1200 Four Color Flexo Press（1200MM） HD-400 Automatic Food Paper Bag Making Machine YT2600 2-COLOR FLEXO PRESS Total 1, Delivery time: within 50workdays to finish the machine production after reciving 30% payment 2, Country of Origin: China 3, Payment Term:30% TT in advance, 70% balance before shipment 4,Warranty: 1 year limited warranty after installation. Bank Information BENEFICIARY: WENZHOU CHANGS INTERNATIONAL BENEFICIARY BANK： CHINA CONSTRUCTION BANK WENZHOU BRANCH SWIFT：PCBCCNBJZJW BENEFICIARY A/C NO.： 33014013100229004101 | 1Set 1SET 1SET 1SET | EXWORK USD48800.00 USD29000.00 USD44950.00 USD8250.00 | USD48800.00 USD29000.00 USD44950.00 USD8250.00 USD131000.00 |

MULTILAYER KRAFT PAPER BAG MAKING MACHINE

Quotation: 48800USD (EX-WORK)

Video: http://v.youku.com/v_show/id_XMTU3NDkwNTQw.html

Main Technical Parameter:

| Bag length: 800-1000 (also can be customize) | Bag width : 300-600mm |
| --- | --- |
| Paper weight : 70-140 gram | Material width: 620-1250mm |
| Speed: 40-60pcs/min | power：11.2KW |
| Kraft paper layers : 2-3layer | Machine weight : 4000kg |

FL-1200 Four Color Flexo Press

Max Paper Width: 1200mm

Quotation: 29000USD (EX-WORK)

Video link: http://v.youku.com/v_show/id_XMjgxNDYyOTQ0.html

HD-400 Automatic Food Paper Bag Making Machine

Quotation: 44950 USD(EXWORK)

Delivery Time: 45 days ESTIMATED

Video: http://v.youku.com/v_show/id_XMjAwMzE0MzY0.html

Specifications:

Cutting Length(C): 150-400mm

Bag Length(H): 140-390mm

Bag Width(L): 80-250mm

Gusset Depth: 10-50mm

Standard Flap: 12-17mm

Speed: 100_300pcs/minPaper Weight: 30-80GSM

Power: 6Kw

Total Weight: 3500KG

Dimension: 4400*1650*1850mm

YT2600 2-COLOR FLEXO PRESS

Quotation: 8250 USD(EXWORK)

Features:

The photo above is just for your reference.

YT Series Double-color Flexograp

Main Technical Parameters：

| Type | YT-2600 | YT-2800 | YT-21000 |
| --- | --- | --- | --- |
| Max. Web Width | 600mm | 800mm | 1000mm |
| Max. Effective Printing Width | 560mm | 760mm | 960mm |
| Range of Repeat Printing Length | 191～914mm | 191～914mm | 191～914mm |
| Max. Diameter of Roll Material | ф450mm | ф450mm | ф450mm |
| Printing Speed | 5～50m/min | 5～50m/min | 5～50m/min |
| Plate Thickness(Both side adhesive tape included) | 2.38mm | 2.38mm | 2.38mm |
| Total Power | 8Kw | 10Kw | 12Kw |
| Overall Dimension | 2300×1860×2145mm | 2300×2060×2145mm | 2300×2260×2145mm |