Add: No20 Dawuji area Liaoyuan industry park Hanyang district Wuhan city Hubei China

Tel: 86-027-84468309                        Cellphone: +86 13627214948

Contact:MS.Wendy Chen                     Fax:86-027-84675883

Web: http://www.whzq.com                    Skype: whzq.wendy

MSN:whzq.wendy@hotmail.com                         Email:cwl@whzq.com / whzq.wendy@hotmail.com

Quotation to WPC granules machine

Purchaser:

Subject: Quotation to WPC granules machine

Email:aigir13@rambler.ru                          Date:Aug 26 2014

Contact Person: Зиннур                           P/L N0. ZQ20140826A

From: Wuhan ZEQI Plastic Machinery Product CO.,LTD

Technology parameters of  WPC(PVC)  granules machine

|  | WPC(PVC) pelletizing line MSSZ62/108 | Set | 1 |
| --- | --- | --- | --- |
| 1 | The host part: Conical twin screw extruder SJSZ 62/108 | Set | 1 |
| a. | Conical twin screw Extruder SJSZ62/108 | Electrical control cabinet | The main motor Converter, Feeding motor Converter. |  |  |
|  |  |  | Japanese ‘INVT’ inverter |  |  |
|  |  |  | Contactor. Air switch ‘CHINT’ products |  |  |
|  |  | Max output | 30-105 kg/h |  |  |
|  |  | Dimensions | 2600mm×1520mm×2450mm |  |  |
|  |  | Overall weight | 2800kg |  |  |
|  |  | Taper of hopper | 10° |  |  |
|  |  | Main power into the line terminal form | Three-phase four-wire |  |  |
|  |  | Motors. Pump manufacturers | Main AC motor 15kw SIEMEN motor | Set | 1 |
|  |  |  | Feeding motor 0.75kw With dehumidifying System |  |  |
|  |  |  | BOSHAN vacuum pump |  |  |
|  |  | Temperature control table. Speed meter supplier | Japanese ‘OMRON’ Intelligence Temperature Controlling Instrument. Digital ammeter, tachometer from Wuhan |  |  |
|  | Die head and flange connection way | Bolt connection |  |  |
|  | Advantages | Good plastcizing, High output, Saving electricity. Rational design of high accuracy.Parts made of high quality materials with homemade processing. Stability, Easy to control. The enterprises and supporting enterprises have passed ISO9001-2000 quality Certification and Electrical accessories by CE Certification. |  |  |
| b. | Screw | Diameter | Ф62mm/108mm | Pcs. | 2 |
|  |  | Effective length | 740mm |  |  |
|  |  | Engaging form | Conical engagement |  |  |
|  |  | Rotational speed | 1-35 r/min |  |  |
|  |  | Nitriding depth | 0.7-0.8mm |  |  |
|  |  | Core of screw heating method | Screw core inner circulation thermostat device |  |  |
| c. | Barrel | Barrel form | Overall type plasticizing | Pcs. | 1 |
|  |  | Heating method | Barrel adopt cast aluminum heater with air-cooled |  |  |
|  |  | Heating sections of the barrel | 2 zones |  |  |
|  |  | Heating power | 10 kw |  |  |
|  |  | Temperature range | 50℃—400℃ |  |  |
|  |  | Cooling medium | Air |  |  |
|  |  | Screw. Barrel quality assurance | For six months |  |  |
|  |  | Nitriding depth | 0.7㎜-0.9㎜ |  |  |
| d. | Transmission speed reduction system | Main drive motor power | 15 KW Three-phase asynchronous motors |  |  |
|  |  | Main drive motor working methods | Δ connected |  |  |
|  |  | Main drive motor speed | 0-1440 r/min |  |  |
|  |  | Reduction gearbox form | Gear box with hard tooth surface helical gear surface-bound form |  |  |
|  |  | Reduction gears | Quenched. Carburizing. Tooth grinding, the material is 20CrMoTi. |  |  |
|  |  | Distribution gearbox form | Two distribution assigned drive shaft rotated by super-cone bevel gear. |  |  |
|  |  | Main drive motor speed control mode | AC frequency control |  |  |
| 2 | Auxiliary machine for WPC (PVC) Granules QL182-2 |  |  |
| a. | Pelletizing die head | Set | 1 |
|  | The adaptation SJSZ62/108 extruder. The die head is made of alloy steel 38CrMoAlA, with special treatment by extension and nitrided, made the die head anti high temperature and anti rust. All the part connect by screw, for easy maintenance. |  |  |
| b. | Pelletizer device: |  |  |
|  | Pelletizer head according to the needs of vertical adjustment , the use of three flexible cutter , the effective protection of the feed plate . |  |  |
| c. | Two - steps air conveying system: |  |  |
|  | This extrusion line adopts 1.5kw×2 fans, through three groups stainless separation device to get material in three installments conveying air from the cooling purposes. The device pipeline separation devices are made of stainless steel , beautiful atmosphere, durable. |  |  |

Origin and brand of electric appliances of MSSZ97/132-QL182-3 and MSDJ 120/25-YF300

- Main motor: SIEMENS

- Contactor: CHINT

- Temperature Controller: OMRON

- Inverter made: INVT

Price: FOBwuhan USD25,000.00

Note: This price is in tax, quotes are valid for 45 days.

Terms of payment: 30% for deposited, 70% paid before shipment by T/T.

Delivery time: 40 days after receipt advance payment.

Packing : Simple package with plastic film (or according to customer's demand, but

the cost is borne by the buyer).

Warranty: Barrel & screw with six months warranty. Other parts warranty period is 1

year. A year later, if replacement parts can be purchased from our

Company.

The service we provide for you

- Provide equipment type selection and technology parameter according user

Product.

- Provide foundation drawing to install equipment. And sent 1 or 2 technicians

responsible for equipment installation guide.

- Provide facilities maintenance and technical skill training for user. These machine

require three people for Commissioning. Debugging time of the machine is about

10 -15days after the customer to complete the preparatory work.

(But the buyer shall pay the commissioning of equipment fee of engineers USD

$80/day/person, and required to provide our technical staff to round-trip air fare

room, board, and other expenses).

- Warranty in the contract for the buyer of quality problems caused by man, the

supplier promised to solve the problem first, and then clearly define the

responsibilities, bear the expense by the responsible party, (material

costs,Traveling costs).

5. Provide turn-key project for user.